## Slide 1
NuFact 02 meeting at Imperial College, London 1 – 6 July 2002
A design development on Liquid Hydrogen Absorber Window
by
Wing Lau, Stephanie Yang
Oxford University

## Slide 2
Outline of this presentation:
How good does the Bellow Window design behave compared with the Torispherical Window design;
A discussion on the buckling behaviour and its effect on structural safety;
A further look at the Fluid Flow comparison between the two design

## Slide 3
FEA predicted burst pressure at design geometry
117 psi
156 psi
FEA predicted burst pressure at as-built geometry
162 psi
123 psi
Window 4 tested at 80K – burst at 152 psi
Window 2 &3 tested at room temp – burst at 120 psi
A brief review of what have been done so far:
Comparing simulation results with test results
  A series of FEA studies have been carried out on the previous Window design and results compared very closely with the test results

## Slide 4
Re-design the Window geometry to reduce its material thickness without compromising its duty rating
A “Bellow” shape window was develop based on the following principles
  Choosing a mid cap size to suit space requirement –
    A spherical shell with the least possible radius to suit the space requirement is used at the centre. This will reduce the shell thickness
  Work out the thickness increment, i.e. the tapered thickness requirement –
    At the “truncation” line of the sphere where the end cap is cut, it should have a thickness sufficient enough to compensate for the stress increase due to the restraint free effect at the rim. This provides a guideline for the tapering requirement
  Provision of a rigid “bridging” piece for the mid-cap to the flange –
    A bellow in the shape of an open toroid of sufficient rigidity is provided to “bridge” the end cap to the inner diameter of the flange. The rigidity of this bellow is such that it should provide the end cap with a near “fully fixed” boundary condition.

## Slide 5
Repeating the Finite Element analysis on the new Window design:
A series of design iteration were carried out to derive the minimum Window thickness which maintains the window at its designed pressure rating
Radial dist from centre
thickness

## Slide 6
A 22cm Absorber Window with 0.03mm machining allowance under internal pressure – Window not burst at 136 psi pressure
Further FEA results on the Bellow Window design
Min. pressure thickness is 0.13mm.
FE model thickness is 0.16mm

## Slide 7
A 34cm Secondary Window with no machining allowance under internal pressure – Window burst at 78 psi
Min. pressure thickness is 0.13mm
FE model thickness is 0.13mm

## Slide 8
A 34cm Secondary Window with 0.05mm machining allowance under internal pressure – Window burst at 112 psi cf 75 psi
Min. pressure thickness is 0.13mm
FE model thickness is 0.18mm

## Slide 9
Xi
t
Window diameter
Specify Window diameter in Cell B2, machining tolerance in Cell D2 & state "V" or "A" in Cell F2 |  |  |  |  |  |  | 
Window diameter in mm:- | 340 | Machining tolerance (mm):- | 0 | Is it the Vacuum (V) or Absorber (A) Window? | v |  | 
Information on the Window geometry (see attached diagram for notation):- |  |  |  |  |  |  | 
R1= | 158.667 | R2= | 161.333 | R3= | 108.191 | R4= | 115.679
X1= | 0.000 | X2= | 0.000 | X3= | 158.667 | X4= | 170.000
Y1= | 0.000 | Y2= | -2.539 | Y3= | 215.333 | Y4= | 215.333
 | Concave Surface |  | Convex Surface |  | thickness // to beam
Xi | Theta = | yi (mm) | Theta= | yi (mm) | t (mm)
0 | 0 | 158.667 | 0 | 158.794 | 0.128
5 | 0.0315 | 158.588 | 0.031 | 158.717 | 0.129
10 | 0.0631 | 158.351 | 0.062 | 158.484 | 0.133
15 | 0.0947 | 157.956 | 0.0931 | 158.095 | 0.139
20 | 0.1264 | 157.401 | 0.1243 | 157.550 | 0.149
25 | 0.1582 | 156.685 | 0.1556 | 156.845 | 0.161
30 | 0.1902 | 155.805 | 0.187 | 155.980 | 0.176
35 | 0.2224 | 154.758 | 0.2187 | 154.952 | 0.194
40 | 0.2549 | 153.542 | 0.2505 | 153.757 | 0.215
45 | 0.2876 | 152.152 | 0.2827 | 152.391 | 0.240
50 | 0.3206 | 150.583 | 0.3151 | 150.851 | 0.268
4. Produced an EXCEL file which calculates the new Window profiles without the need to use any CAD facilities
55 | 0.354 | 148.829 | 0.3479 | 149.130 | 0.301
60 | 0.3878 | 146.885 | 0.3811 | 147.222 | 0.337
65 | 0.4221 | 144.742 | 0.4147 | 145.121 | 0.379
70 | 0.4569 | 142.391 | 0.4488 | 142.817 | 0.426
75 | 0.4923 | 139.822 | 0.4835 | 140.301 | 0.480
80 | 0.5285 | 137.022 | 0.5188 | 137.562 | 0.540
90 | 0.6031 | 130.672 | 0.5918 | 131.358 | 0.686
95 | 0.6419 | 127.083 | 0.9416 | 127.858 | 0.775
100 | 0.9209 | 123.237 | 0.9977 | 124.429 | 1.192
105 | 0.9741 | 119.643 | 1.0518 | 121.390 | 1.748
110 | 1.0255 | 116.431 | 1.1042 | 118.706 | 2.275

## Slide 10
Additional analysis required on the Secondary window
The secondary needs to withstand an external pressure of 25 psi. Here is the design requirements received from the FERMI Safety Committee
1) Perform an external pressure test on each vacuum window to 25 psid to demonstrate no failures will result; i.e. no creeping, no yielding, no elastic collapse/buckling, no rupture.
(2) Vacuum system internal pressure test (maximum test pressure = 37.5 psid) per UG-100 of the ASME Section VIII of the Pressure Vessel Code.
(3) Vacuum system "Pressure and Decay Test" to an internal pressure of 37.5 psid for MuCool configuration. Pressure is held for 30 minutes. The test must demonstrate that no failures will result to the windows; i.e. no creeping, no yielding, no elastic collapse/buckling. This is essentially the same as (3). See guidelines II.D.4.c.(i).
(4) Vacuum system Leak test. No leaks may be seen using a helium leak detector on a scale with a minimum sensitivity of 10E-9 atm-cc/sec.

## Slide 11
The interpretation of buckling and its implication
In general, there are two types of buckling modes:-
The local buckling –
This could be caused by a weak spot in the structure. This may or may not affect the structural integrity of the component. To demonstrate the acceptability of this, we need to prove that:
  the deformation can be fully reversed on the removal of the applied load;
  no permanent deformation occurs – i.e. stress are below yield;
The general buckling load –
This will lead to a snap through scenario. Its excessive deflection, and stresses will lead to permanent deformation. It would not be possible to recover its original shape even after the removal of the applied load. A general buckling is not accepted under any circumstance.

## Slide 12
The buckling analysis of the 34cm Vacuum Window with 3 different thicknesses:
Our first approach was to calculate the bifurcation load (linear buckling load) using an Eigenvalue solution. A 3-D model was set up to conduct the analysis and the results are as follow:-
0.13 mm thick
Local buckling pressure = 5.43 psi
0.18 mm thick
0.23 mm thick
Local buckling pressure = 15.3 psi
Local buckling pressure = 27 psi
This approach resulted in very low buckling load because it does not reflect the change in stiffness due to the geometry changes. A better approach is to perform the non-linear analysis of the structure under an incremental external load

## Slide 13
A non-linear 2-D axisymmetrical model with incremental external load
General buckling developed at about 55 psi
Local buckling detected at 54 psi
No buckling at 52 psi
The 0.13mm thick window

## Slide 14
A non-linear 2-D axisymmetrical model with incremental external load
Formation of local buckling at 55 psi
General buckling at 75 psi
The 0.18 mm thick vacuum window

## Slide 15
A non-linear 2-D axisymmetrical model with incremental external load
Buckling pressure at 104psi – stresses are just below yield prior to buckling
No local buckling detected
The 0.23 mm thick Vacuum window

## Slide 16
A non-linear 3-D model with incremental external load – window thickness is 0.23mm

## Slide 17
Fluid Flow analysis
The FE fluid model used in the analysis

## Slide 18
Comparison of the flow performance between the Bellow & the Torispherical Windows
The following model and flow conditions were run
 | Water at |  | LH2 at | 
Torispherical Window | 24 m/s | 5 m/s | 2 m/s | 5 m/s
Bellow Window | 2 m/s | 5 m/s | 2 m/s | 5 m/s

## Slide 19
Flow velocity at 5 m/s
Flow velocity increased to 24 m/s
Flow velocity at 5 m/s
Water flow pattern at the 2 Windows

## Slide 20
LH2 flow pattern at the 2 Windows
Flow velocity at 5 m/s
Flow velocity at 5 m/s

## Slide 21
The follow conclusions on the fluid performance of the Windows were drawn
The above analyses demonstrated that the contour adopted by the Bellow Window allows a better flow pattern to be developed than the Torispherical Window does;
At a relatively low flow speed (5m/s), the fluid in the Bellow Window was able to reach the Window thereby allowing a better heat transfer from the Window to the fluid
It is important that the fluid be directed to the Window boundary in the shortest time so that any heat developed in the metal could be absorbed and transported away. If this is not done in a timely manner, it would cause local LH2 to boil which could lead to higher pressure being built up inside the Window;
Further analyses are needed to study how the flow pattern develops at higher flow velocity.

## Slide 22
So, how good is the new window design?
It is at least more than 40% thinner than its torispherical version without having to change to the more exotic materials;
All the linear scaling rules apply. The geometry profile of any window dimension can be extrapolated upsize or downsize from a standard design model knowing that it would reach the design pressure rating without the need for further FEA substantiation;
The new window profile performs better fluid dynamically.