International Linear Collider Calorimeter Test Beam Program

J. C. Brient and J. Yu

For the ILC Calorimeter Test Beam Group

Abstract

The linear collider requires an excellent detector performance to fully exploit its physics potential. In particular, hadronic jet energies need to be measured with unprecedented resolution of 30%/√E or better. To meet this challenge, novel technologies are being developed which need to be tested with particle beams. With the recent decision by the International Technology Recommendation Panel (ITRP), the time scale for detector development demands basic detector design choices to be made within the next few years. To meet this time scale for the development of calorimetry, the international linear collider test beam group is submitting this MOU to Fermilab. The main goals of this test beam program are to evaluate the different choices of technologies proposed for the calorimeter and to understand, validate and improve the Monte Carlo modeling and simulation of hadronic showers. This document contains a request for test beams from fourteen distinct calorimeter and muon-detector/tail-catcher groups. This proposal lays out a preliminary MOU for a test beam program including time scales and institutional responsibilities. It requests Fermilab to provide access to the Meson Test Beam Facility, upgrades to particle energy ranges and intensities, and associated engineering and computing support services.

Draft 4.0

December 1, 2004

Abstract

I.	Physics justification for testing calorimeter prototypes for the linear Collider Detector	3

II.	Calorimeter technologies in consideration	6

Iii.	Proposed test Program	11

iV.	personnel and institutions	14

V.	requirements: beam composition, energies, rates	16

VI.	requirements: floor space, infrastructure	18

VII.	responsibility by institutions - Non-Fermilab	19

VIII.	RESPONSIBILITIES BY INSTITUTION - FERMILAB	20

8.1	Fermilab Beams Division

8.2	Fermilab  Particle Physics Division

8.3	Fermilab  Computing Physics Division

8.4	Fermilab ES&H Section

IX.	Access to data                                                                                      22

X.	SPECIAL CONSIDERATIONS		 			  	23

XI.	Bibliography									25

XI.	SIGNATURES								26

APPENDIX I - Hazard Identification Checklist

I. Physics Justification for Testing Calorimeter Prototypes for the Linear Collider Detector

The detectors at the International Linear Collider (ILC) are envisioned to be precision instruments that can measure Standard Model physics processes near the electroweak energy scale and discover new physics processes beyond it.  In order to take full advantage of the physics potential of the ILC, the performance of the detector components comprising an experiment must be optimized, sometimes in ways not explored by the previous generation of collider detectors. In particular, the design of the calorimeter system, consisting of both electromagnetic and hadronic components, calls for a new approach to achieve the precision required by the physics.  As a precision instrument, the calorimeter will be used to measure jets from decays of vector bosons and heavy particles, such as top, Higgs, etc.  For example, at the ILC it will be essential to identify the presence of a Z or W vector boson by its hadronic decay mode into two jets, requiring a dijet mass resolution of at least ~3 GeV or, equivalently, a jet energy resolution σ/E ~ 30%/(E.  None of the existing collider detectors has been able to achieve this level of precision.

Preliminary studies indicate that a jet energy resolution of ~ 30%/(E can be obtained by the application of Particle-Flow Algorithms (PFAs) [1]. PFAs use tracking detectors to reconstruct charged particle momenta (~60% of jet energy), electromagnetic calorimetry to measure photon energies (~25% of jet energy), and both electromagnetic and hadronic calorimeters to measure the energy of neutral hadrons (~15% of jet energy).  To fully exploit PFAs, the calorimeters must be highly granular, both in transverse and longitudinal directions, and  thus allow for the separation of the energy deposits from charged hadrons, neutral hadrons, and photons in three spatial dimensions. For this reason, the optimization of the calorimeter designs for the application of PFAs is absolutely critical to accomplish the physics goals of the ILC.

The developments of PFAs, on the other hand, rely entirely on Monte Carlo (MC) models. Their performance depends critically on the details of the hadronic showers, such as the production of secondaries, the interparticle distances, the energy deposition in thin layers, etc..

At present a number of different models [2-5] simulating the hadronic shower development exist. These models differ significantly in several important aspects. To give an example, Figure 1, taken from a presentation by G Mavromanolakis [6], compares the predicted shower radius for fifteen different MC models of the hadronic shower. Differences of up to 60% are seen. However, at present there is insufficient experimental data to distinguish between these models. To remedy this situation a large part of the proposed test beam program will be devoted to the detailed measurement of hadronic showers and to the validation of these models.

The design of a precision calorimeter for the ILC detector requires the development and testing of new detector technologies. Tests of several concepts of the electromagnetic calorimeter (ECAL) in standalone mode with emphasis on the analog energy measurement of electromagnetic showers are necessary.  Here the challenge is to minimize the lateral extent of showers with a dense ECAL, as required for the optimal use of PFAs, while preserving a good energy resolution.  In addition, novel electronics and schemes for the readout of the active media of these calorimeters need to be tested in a beam environment.

Figure 1. Comparison of the shower radius in a hadronic calorimeter as predicted by fifteen different MC models of hadronic showers. Differences from a few % to as large as 60% between different models can be seen.

For the hadronic calorimeter (HCAL), the requirement of fine grain segmentation has prompted consideration of digital as well as analog readout schemes for several sensitive gap technology choices. The development of a digital HCAL is fairly new and requires standalone testing to validate the unique (to calorimetry) technologies under consideration. Gas detectors (Resistive Plate Chambers [7] and Gas Electron Multipliers [8]) are being explored as active medium. The proposed analog HCAL utilizes scintillator tiles as small as 3 x 3 cm2 together with a novel electronic readout device mounted directly on the side of the tile. To extend the longitudinal range of detailed measurements of hadronic showers, the tests of the HCAL need to include a muon-detector/tail-catcher located in the back of the HCAL. Two distinct technologies for this device will be tested in this program as well. Furthermore, a prototype muon-detector/tail-catcher will provide data essential for developing effective strategies in dealing with energy leakage from relatively thin calorimeters as are being imagined for the ILC

Finally, to validate Monte Carlo models used to develop the PFAs, the entire calorimeter, consisting of ECAL and HCAL, needs to be tested in a wide variety of test beam configurations, including hadron energies as low as 1 GeV, electron energies as high as 25 GeV, and several angles of incidence and impact points.  As an alternative to the use of MC models, the test beam data will be used to generate extensive libraries of hadronic showers.  Collecting a comprehensive data set with unprecedented granularity to provide a reference for further improvement of hadronic shower modeling is of paramount importance for the design of a detector for the ILC. Independently of the ILC, the proposed measurements are also valuable in their own right, since they further the understanding of both calorimetry and hadronic showers.

In addition to the wide range of technical benefits laid out above, we anticipate 10 – 20 publications from this effort.  This document also provides a detailed plan requested in the recommendation [9] by the DESY Physics Research Committee (PRC) at its meeting in May 2004, which endorsed the general need for linear collider test beam program.

II. Calorimeter Technologies To Be Tested

In order to develop a complete calorimeter system for linear collider detectors, it is necessary to build and test three components: electromagnetic calorimeter (ECAL) modules, hadron calorimeter (HCAL) modules, and an integrated ‘tail-catcher’ and muon system to be located behind the ECAL and HCAL.

For the electromagnetic modules, two designs using silicon as the active medium between tungsten plates are being developed: one in Europe and one in the U.S. These two designs differ in the degree of integration of the readout electronics on-board each active layer and in their transverse segmentation. Two further designs use scintillator as the active medium, one from the U.S. with half-offset tiles, and the other from Japan. Finally, there are two hybrid electromagnetic calorimeter designs, one from the U.S. using silicon/scintillator with tungsten absorber and one from Italy using silicon/scintillator with lead absorber.

The HCAL modules to be tested include both analog and digital approaches. A joint U.S.-European design uses scintillator and steel absorber with analog readout. The two digital hadron calorimeter designs, one from the U.S./Russia, using resistive plate chambers (RPC) as the active medium and the other, a U.S.-China effort, using gas electron multiplier (GEMs) charge amplification layers, both use steel absorber.  Other dense absorber materials, such as Tungsten, are also in consideration.

The muon-system/tail-catcher has two designs, a CALICE (primarily DESY and NIU) scintillator-steel option, and a RPC-steel option from Italy.

A significant part of the design and construction of the prototype calorimeters is borne by the CALICE collaboration [10], currently a group of 24 institutes located in seven different nations. From the U.S., groups at Argonne National Laboratory, Northern Illinois University, and University of Texas at Arlington are full members of the collaboration.

2.1 Electromagnetic Calorimeters

2.1.1 Silicon - Tungsten

As discussed above, PFAs require a highly segmented electromagnetic calorimeter (ECAL). A natural way of implementing this is with alternating layers of tungsten (W) and silicon (Si) detectors, combining the small Molière radius of W with Si detectors readily segmented into pixels of 1 x 1 cm2 or 0.5 x 0.5 cm2. The longitudinal profile will consist of about 30 layers each of thickness 1 to 5 mm, depending on the eventual optimization.

Two groups, the CALICE collaboration and a group from Brookhaven, Oregon, and SLAC (BOS), are working on the design of such an ECAL. A major challenge is to integrate the electronics into the detectors, providing an effective reduction in the number of readout channels by a large factor (of order 1000). Maintaining a small Molière radius requires that the readout gap, including Si detectors and the readout electronics, be kept extremely thin (( 1 mm). The implementation of such a system differs between the two groups mentioned above, but both are novel and will require testing in a beam. In the BOS case, both analog and digital readout is performed on a single ASIC which is bump-bonded to the Si detectors. The Si detectors themselves have metallizations which carry the signals from individual pixels to the ASIC. The CALICE system is still being designed, but will also be highly integrated in its final form.

A test beam with electrons of modest energy ((20 GeV) is required to evaluate the new technologies in standalone tests of these ECAL modules. As a separate function the test module will provide a radiator simulating the actual ECAL, with close to the correct segmentation, for the validation of hadron showers in the test beam program. For this function, it is not necessary that the Si-W include the innovations mentioned above. In fact, CALICE is well along in the fabrication of such a Si-W test beam module. This is a full-depth module and will be used for the first round of hadron shower measurements, until the integrated designs become available.

The CALICE ECAL effort is funded for construction of prototype and beam test while the U.S. effort is not funded beyond detector R&D.  Therefore, the time scale for U.S. ECAL beam test is not as certain.

2.1.2 Scintillator – Tungsten

A technology is being studied by the University of Colorado group where alternate layers are offset by half a tile width from each other. In this manner 5 x 5 cm2 tiles have an effective area of 2.5 x 2.5 cm2 and this improves the spatial resolution. This array is being simulated to determine the improvement in spatial resolution. At the same time we have the best energy resolution possible which is characteristic of scintillator based calorimetry. This effort is currently not funded sufficiently for construction of prototype and beam test.

Independently, a group from Japan is developing a scintillator strip based design, using 3mm tick tungsten plates.  Each sensitive layer consists of 20 pieces of strips of size 1cm (W) x 0.2cm (T) x 20 cm (L) in x and y directions, providing 1 cm x 1 cm effective cell size. A prototype with 38 layers will be prepared for test beam program.

2.1.4 Hybrid technologies

Two groups are developing a compact hybrid EM calorimeter. Under consideration are sandwich designs with thin Tungsten or lead as the absorber. The sampling will be done by thin layers of scintillator-tiles with WLS fiber readout to on-tile B-field tolerant photo-detectors (eg. Silicon-Photo-Multipliers, SiPMs [11]) and by a number of layers of silicon with small pads or strips with an area around 1 cm2.

The major cost-driver to the Si-W approach discussed in the previous section is the extended area of silicon. This hybrid approach could lead to an ECAL which meets the necessary EM resolution more cost effectively, while still addressing the granularity requirements at large radius. Most of the proof-of-principle technological R&D is in progress by the proponents of the silicon and scintillator approaches.

The concept of a cost-effective solution to a high-granularity ECAL is particularly interesting to overall detector design concepts with large volume gaseous tracking and large ECAL radius.

The European group which consists of Como, ITE-Warsaw, LNF, Padova, and Trieste has already explored with test beams, a design, LC-CAL [12], using lead as absorber and three layers of Silicon readout. The Kansas/Kansas-State University groups are investigating the design of an EM calorimeter with substantial sampling by the Silicon layers.

The proposed design of a hybrid sampling ECAL is rather novel and needs test-beam demonstration of performance both as a standalone ECAL and as part of a calorimeter system measuring hadronic particles. The relative sampling by the scintillator and silicon readout needs to be optimized with test-beam data.

2.2 Analog/Semi-Digital Hadron Calorimeter

2.2.1 Scintillator – Steel

The CALICE Collaboration is pursuing the development and construction of a scintillator-steel, cubic meter size, hadron calorimeter prototype [13]. The prototype design envisages the construction and testing of a finely-grained hadron calorimeter using a proven technology for the active medium in combination with novel solid-state photo-detectors. The proposed prototype consists of 38 layers of 5 mm thick scintillator tiles sandwiched between 2cm thick steel absorber plates mounted on a movable stand. The stand is designed to hold both ECAL and HCAL modules and to position them in any direction with respect to the incident beam.  The prototype geometry, based on a solid foundation of hardware R&D and simulation studies, will be able to address the goals of technology demonstration, hadron shower MC validation and particle flow algorithm development. The hardware R&D has included detailed tests of tile-fiber optimization, photo-detector characterization and the operation of a 100 channel MINICAL in a low energy electron test beam [14] at DESY while the simulation studies have involved the development of innovative algorithms for shower separation, energy reconstruction and particle flow in the analog and digital environments.

The first thirty layers of prototype have a 30 x 30 cm2 core instrumented with 3 x 3 cm2 tiles, followed by tiles of 6 x 6 cm2 and 12 x 12 cm2 as one moves out laterally from the center of the layer. The last 8 layers are instrumented with only the 6 and 12 cm tiles. Each tile has a wavelength-shifting fiber mated to a solid-state photo-detector (Silicon Photomultiplier) sitting on board. The Silicon photo-multiplier is a multi-pixel avalanche photo-diode operated in the limited Geiger mode. The output signal is the analog sum of the binary single pixel signals and thus proportional to the light intensity with the dynamic range being set by the total number of pixels (~ 1000). Due to its small size, high gain and low operation voltage, the device is ideally suited to be mounted directly on scintillator tiles, thus avoiding the mechanical complications and light losses associated with optical fiber routing for a large number of channels.

The prototype granularity has been chosen to meet the following criteria:

- “Digital”  Hadron Calorimetry:  Monte Carlo studies have indicated that scintillator cells of size 3x3 cm2 can be used in the digital or semi-digital modes i.e. with one or two-bit resolution of the readout. Scintillator as active medium provides the flexibility to trade between granularity and dynamic range. With this prototype we will be able to explore the whole range of readout from the purely digital to the fully analog and arrive at a detector optimized for performance and cost.

- Shower separation: In the PFA paradigm it is particularly important to disentangle the contributions of neutral and charged hadrons efficiently and accurately in a dense environment.

The scintillator HCAL effort is driven by the CALICE collaboration, in particular the institutes from Czech Republic (Prague), Germany (DESY and Hamburg University), Russia (ITEP, JINR, LPI, MEPhI), France (LAL), UK (Imperial, RAL, UCL) and the US (NIU).

2.3 Digital Hadron Calorimeters

2.3.1 Resistive Plate Chambers – Steel

Resistive plate chamber (RPC) are being explored as the active medium of a digitally readout hadron calorimeter. They are based on a simple concept and provide high particle detection efficiency, low noise rates, good position and timing resolution, and low construction cost.  R&D efforts showed that the technology based on glass as resistive plates is reliable.  Tests of a prototype hadron calorimeter section based on RPCs with digital readout in a particle beam will prove the technology, measure hadronic showers with unprecedented spatial resolution and validate Monte Carlo modeling of hadronic showers.  The proposed prototype test section is 1m x 1m x 1m in size and features 38 layers of 1m x 1m x 20mm steel absorber plates interleaved with 1m x 1m x (6–8)mm active layers (RPC and readout board).  The RPCs will be readout digitally with 1x1 cm2 lateral segmentation. The total number of readout channels is 400,000.  The electronic readout system will be built around a front-end ASIC, which is currently being developed.

The effort is being borne by groups at Argonne National Laboratory (member of CALICE), Boston University, University of Chicago, Fermilab, and University of Iowa.

2.3.2 Gas Electron Multipliers – Steel

This technology uses gas electron multiplier (GEMs) [11] foils in an Argon/CO2 filled volume as the active medium. Charged particles crossing an ionization region release electrons. The electrons drift in an electric field to a multiplication structure composed of two GEM foils. A gain of at least several thousand is achieved. The final electrons are collected on 1cm x 1cm anode pads, which are connected to a charge preamplifier and discriminator. The output is then a “yes” or no as to whether a hit is recorded for a given channel. The readout electronics, both the analog amplification and the digital signal processing, will be handled by an ASIC being jointly developed with the RPC digital hadron calorimeter group at ANL and Fermilab PPD. It is foreseen that the testbeam stack will comprise 38 active layers and the same number of 20 mm steel absorber plates. Each layer will be approximately 1 x 1 m2 in area, and 8 - 9mm thick. In order to maintain the flatness and geometrical integrity of each active layer, part (~2mm) of the absorber will be used as a “strongback” upon which each layer will be assembled. The anode pads will be an integral part of the PC board forming the readout layer. The 64-channel ASIC’s will be mounted at intervals across each PC board. The ASIC’s will have a changeable gain: high for the smaller GEM signals, and low for the higher RPC signals. Each active layer will be divided into three sections of approximately 1m x 0.3m dimensions due to the available sizes of GEM foils and PC boards.

The project involves University of Texas at Arlington (a member of CALICE) and University of Washington.

2.4 Muon detectors/Tail Catchers

CALICE collaboration is pursuing the construction of a cubic meter sized scintillator-steel device which will serve as both a tail-catcher and muon tracker (TCMT). The TCMT prototype, designed with this dual purpose in mind, will have a fine and coarse section distinguished by the thickness of the steel absorber plates (2cm and 10 cm respectively). The fine section sitting directly behind the hadron calorimeter and having the same longitudinal segmentation as the HCAL, will provide a detailed measurement of the tail end of the hadron showers. This measurement is crucial to the validation of hadronic shower models, since the biggest deviations between models occurs in the tails. The subsequent coarse section will serve as a prototype muon system for any design of a Linear Collider Detector and will facilitate studies of muon tracking and identification within the particle flow reconstruction framework. Additionally, the TCMT will provide valuable insights into hadronic shower leakage and punch-through from thin calorimeters and the impact of the coil in correcting for this leakage.

There will be a total of 16 layers (8 fine and 8 coarse) in the TCMT. Extruded scintillator strips, with wavelength shifting fibers mated to SiPM readout, will serve as the active media. The strips will be 1m long, 5cm wide and 5mm thick. These dimensions have been determined based on Monte Carlo studies focused on both calorimetric and muon reconstruction issues. The strips will be oriented perpendicular to each other in successive layers. The TCMT will sit in its own movable cart capable of forward-backward and sideways motion and will use the same electronics as the scintillator-steel hadron calorimeter.  The construction of this device is being pursued by CALICE with the engineering contributions from Fermilab.

In addition, the Frascati group is developing a TCMT based on glass RPCs. The RPCs feature a single gas gap and are operated in avalanche mode.

III. Proposed Test Program

There will be three different parts to the testing program. Due to early availability the testing will initiate with electromagnetic calorimeters, followed by standalone tests of hadronic calorimeters including tail catchers, and conclude with combined tests of electromagnetic and hadronic calorimeters. As more prototype calorimeters, both of ECAL and HCAL type, become available, the cycle of standalone followed by combined tests will be repeated. Tests with large, high field magnets are under discussion and will be proposed at a later stage.

We propose to collect of the order of 106 events per setting (particle type, energy, angle, and technology), leading to a grand total of the order of 108 events for all proposed measurements. The 106 events per setting are needed to achieve a statistical precision of better than 1% per bin, taking into account effects of beam spot size, beam momentum spread, contamination from other particles in the beam, and for providing sufficient statistics to subdivide the data sample. The large sample sizes are needed not only to allow tighter beam selection, to minimize systematic uncertainties, but also to analyze the hadron shower data as a function of observables which cannot be pre-configured, like the electromagnetic energy fraction, the number of hadronic interaction vertices, or the longitudinal and lateral containment. Such studies are needed for the optimization of both the single particle energy reconstruction using weighting methods, as well as for particle flow algorithm development. A 1% statistical precision is needed to distinguish between currently available models of hadronic showers which typically differ by 10% for observables, such as shower radius and energy deposition.

3.1 Standalone tests of electromagnetic calorimeters

For the different choices of ECAL technologies the response of the prototypes will be measured in the following configurations:

▪ Energy Scans with Electron Beams: Depending on the available energy range of electrons, between 5 and 10 energy points will be measured to establish the linearity of the response and the energy resolution. Also, low energy (<7 GeV) measurements will be used to cross-check with previous measurements performed at DESY.

▪ Incident Angle Scans: Measurements with at least three different angles of incidence will be performed.  These tests are foreseen using at least two different energy settings.

▪ Hadronic Shower Development in the ECAL: Measurements with and without one or two blocks of Tungsten, each ~0.9 λI deep will be performed using low-energy (<10 GeV) hadron beams. These tests will provide detailed measurements of hadronic showers, taking advantage of the fine granularity of the ECAL prototypes and the high resolution readout.

The first prototype calorimeter (the CALICE ECAL) will be ready for tests by summer 2005 [15]. Prototypes based on the other technologies will be available by summer 2006 at the earliest, while pre-prototypes might be tested at an earlier date.

3.2 Standalone tests of hadronic calorimeters including tail catchers

Standalone tests of prototypes of the hadronic calorimeter will be performed in the following configurations:

▪ Energy Scans with Pions and Protons: Single pion responses, linearity and energy resolution will be measured using a wide range of energies (as low as possible below 3 GeV up to 66 GeV). The response to protons over the entire momentum range (up to 120 GeV) will be measured as well.

▪ Incident Angle Scans: Measurements with at least three different angles of incidence will be performed.  These tests are foreseen using at least two different energy settings.

▪ Muon Responses: Measurements with momentum tagged (3 – 20 GeV/c)  muons will be performed for testing reconstruction codes and developing calorimeter tracking algorithms.

▪ Calibration Runs: For calibration purposes, measurements with defocused muons need to be performed at regular intervals during the testing period.

The first prototype hadronic calorimeter (CALICE tile-cal) and scintillator based tail catcher will be ready for tests by fall of 2005. Prototypes based on the other technologies (RPCs and GEMs) will be available by 2006, possibly preceded by tests of pre-prototypes. Figure 2 shows a schematic diagram of the CALICE hadronic calorimeter movable stand.  The overall width of the stand is 5 m with a 2.8 m movable part to maintain a 1 m horizontal move.  The 2.8m movable part width is to accommodate 1.3m detector dimension with a 1 m to slide active layers in and out of the prototype, and the remaining space is taken up by the mechanical support structure to rotate the active layers in horizontal position for cosmic ray data taking.

3.3 Combined test of electromagnetic and hadronic calorimeters including tail catchers

The following test program is foreseen for the various combinations of ECAL and HCAL prototypes:

▪ Electron Energy Scans: These tests require electrons with the highest achievable energy, to provide a data set with combined ECAL and HCAL information.

▪ Energy Scans with Pions and Protons: Single pion responses, linearity and energy resolution will be measured using a wide range of energies (1 – 66 GeV). The response to protons over the entire momentum range (up to 120 GeV) will be measured as well.

▪ Incident Angle Scans: Measurements with at least three different angles of incidence will be performed.  These tests are foreseen using at least two different energy settings.

▪ Muon Responses: Measurements with momentum tagged (3 – 20 GeV/c) muons will be performed for testing reconstruction codes and developing calorimeter tracking algorithms.

▪ Calibration Runs: For calibration purposes, measurements with defocused muons need to be performed at regular intervals during the testing period.

The combined tests will start in the winter of 2005 and last until approximately the end of 2008.

3.4 Summary of the proposed test program

The proposed test program and associated time scales is summarized in Table 1

|  | 7 – 12/2005 | 1 – 6/2006 | 7 – 12/2006 | 1 – 6/2007 | 7 – 12/2007 | 2008 |
| --- | --- | --- | --- | --- | --- | --- |
| CALICE ECAL | X |  |  |  |  |  |
| Other ECALs |  |  | X | X |  |  |
| CALICE HCAL | X | X | X |  |  |  |
| Other HCALs |  |  | X | X | X |  |
| Combined tests | X | X | X | X | X | X |

Table 1. Time scale of the ILC test beam program for various detector systems and technologies.

IV. Personnel and Institutions

The following Tables 2.a and 2.b list all participating institutions and the names of the physicists involved in the test beam program at Fermilab.

Table 2.a Part one of the list of institutions and personnel participating in ILC calorimeter program.

| Institutions/Collaborations | Personnel Names |
| --- | --- |
| CALICE | Argonne National Laboratory | S.Chekanov, G.Drake, S.Kuhlmann, S.R.Magill, B.Musgrave, J.Repond, D. Underwood, B Wicklund, L Xia |
|  | University of Texas at Arlington | A.Brandt, K.De, V.Kaushik, J.Li, M.Sosebee, A.White, J.Yu |
|  | Northern Illinois University/ NiCADD | G. Blazey , D. Beznosko, D. Chakraborty, A. Dychkant, K. Frances, D. Hedin, D.Kubik, G Lima, R. McIntosh, V. Rykalin, V. Zutshi |
|  | University of Birmingham, UK | C.M.Hawkes, S.J.Hillier, R.J.Staley, N.K.Watson |
|  | Cavendish Laboratory Cambridge University, UK | C.G.Ainsley, G.Mavromanolakis , M.A.Thomson, D.R.Ward |
|  | Laboratoire de Physique Corpusculaire – Clermont | F.Badaud, G.Bohner, F.Chandez, P.Gay, J. Lecoq, S.Manen, S.Monteil |
|  | Joint Institute for Nuclear Research – Dubna, Russia | V.Astakhov, S.Golovatyuk, I.Golutvin, A.Malakhov, I.Tyapkin, Y.Zanevski, A.Zintchenko , S.Bazylev, N.Gorbunov, S.Slepnev |
|  | DESY – Hamburg, Germany | G.Eigen, E.Garutti, V.Korbel, R.Poeschl, A.Raspereza, F.Sefkow |
|  | Hamburg University, Germany | M.Groll, R.-D. Heuer, S.Reiche |
|  | Kangnung National University – Kangnung, Korea | G.Kim, D-W. Kim, K.Lee, S.Lee |
|  | Imperial College London, UK | D. Bowerman, B. Cameron, P. Dauncey, D.Price, O. Zorba |
|  | University College London, UK | S. Bogeert, J.M.Butterworth, D.J.Miller, M.Postranecky ,M.Warren, M.Wing |
|  | University of Manchester, UK | R.J.Barlow, I.P.Duerdoth, N.M.Malden ,D. Mercer, R.J.Thompson |
|  | University of Minsk, Russia | N.Shumeiko, A.Litomin, P.Starovoitov, V.Rumiantsev, O.Dvornikov, V.Tchekhovsky, A.Solin, A.Tikhonov |
|  | Institute of Theoretical and Experimental Physics – Moscow, Russia | M.Danilov, V.Kochetkov, I.Matchikhilian, V.Morgunov, S.Shuvalov |
|  | Lebedev Physics Institute – Moscow, Russia | V. Andreev, E. Devitsin, V. Kozlov, P. Smirnov, Y. Soloviev, A. Terkulov |
|  | Moscow Engineering and Physics Institute- Moscow, Russia | P.Buzhan, B.Dolgoshein, A.Ilyin, V.Kantserov, V.Kaplin, A.Karakash, E.Popova, S.Smirnov |
|  | Moscow State University Moscow, Russia | P.Ermolov, D.Karmanov, M.Merkin, A.Savin, A.Voronin, V.Volkov |
|  | Laboratoire de l'Accélérateur Linéaire – Orsay, France | B.Bouquet, J.Fleury, G.Martin, F.Richard, Ch. de la Taille, Z.Zhang |
|  | LLR - Ecole Polytechnique – Palaiseau, France | M.Anduze, J.Badier, J-C.Brient, A.Busata, S.Cholet, F.Gastaldi,A.Karar,C. Lo Bianco, P.Mora de Freitas, G.Musat, A.Rouge, J-C. Vanel,H.Videau |

Table 2.b Part 2 of the list of the participating institutions and personnel in ILC test beam program.

| Institutions/Collaborations | Personnel Names |
| --- | --- |
| CALICE | Physique des Interfaces et Couches Minces - Ecole Polytechnique – Palaiseau, France | Y.Bonnassieux, P.Roca |
|  | LPNHE - Université de Paris 6 et 7, France | A. Savoy-Navarro |
|  | Charles University – Prague, Czech | S.Valkar, J.Zacek |
|  | Institute of Physics, Academy of Sciences of the Czech Republic – Prague, Czech | J.Cvach, M.Janata, M.Lokajicek, S.Nemecek, I.Polak, J.Popule, M.Tomasek, P.Sicho, V.Vrba, J.Weichert |
|  | Institute of High Energy Physics – Protvino, Russia | V. Ammosov, Yu.Arestov, B.Chuiko, V.Ermolaev,V.Gapienko, A.Gerasimov, Y.Gilitski,V.Koreshev, V.Lishin, V.Medvedev, A.Semak, V.Shelekhov, Yu.Sviridov, E.Usenko, V.Zaets, A.Zakharov |
|  | School of Electric Engineering and Computing Science, Seoul National University | Ilgoo Kim, Taeyun Lee, Jaehong Park, Jinho Sung |
|  | Laboratoire de l'Accélérateur Linéaire – Orsay, France | B.Bouquet, J.Fleury, G.Martin, F.Richard, Ch. de la Taille, Z.Zhang |
|  | Rutherford Appleton Lab., UK | N.K.Watson |
| University of Chicago | M. Oreglia |
| University of Oregon | R. Frey, D. Strom |
| Stanford Linear Accelerator Laboratory | M. Breidenbach |
| University of Kansas | P.Baringer, A.Bean, D. Besson D.Gallagher, C.Hensel, G.Wilson |
| Kansas State University | T. Bolton, E. von Toerne, D. Onoprienko |
| University of Colorado | S. Chen, E. Erdos, U. Nauenberg, M. Nagel, J. Zhang |
| University of Iowa | Y. Onel |
| University of Washington | T. Zhao |
| Fermilab | E. Ramberg, R. Yarema, H.E. Fisk |
| University of Oklahoma | P. Skubic |
| LC-Cal | INFN LNF, Italy | M. Anelli, S. Bertolucci, M. Cordelli, S. Miscetti |
|  | INFN Padova , Italy | E. Borsato, P. Checchia, C. Fanin, M. Margoni, F. Simsonetto |
|  | INFN Trieste , Italy | B. Nadalut, M. Prest,E. Vallazza |
|  | Universita’ dell'Insubria , Como Italy and INFN, Italy | M. Alemi, A. Bulgheroni, M. Caccia |
|  | Institute of Electron Tecnology, Warsaw, Poland | J. Marczewski |
| Shinshu University, Japan | Tohru Takeshita |
| Kobe University, Japan | Kawagoe Kiyomoto |

V. Requirements: Beam composition, energies and rates

A considerable number of different tests are required over an extended period of time. We will have different requirements at different times, and it is our intention to coordinate these needs with gradual improvements in the test beam as much as possible.

Therefore the emphasis will be on electron beams at a range of energies up to the highest feasible energies, perhaps up to  25 GeV/c, and pions and muons over a range of energies, such as a few GeV up to 66 GeV.  There will be a requirement for lower energy pions, down to roughly 1 GeV.

The required rates will be a function of which part of the program is active at a particular time. In general, we need low to moderate instantaneous rates, and high integrated flux, which implies a good duty cycle, i.e. percentage of beam spill time versus total time. This may be accomplished in different ways at different times, e.g. depending on whether NUMI is running or not. Given a 1% duty cycle and a limitation of 100 Hz for data taking, dictated by the data acquisition system and the recovery time of some of the technologies (RPCs), the requested 108 events will necessitate 108 seconds or about 3 years of data taking. Improvements of the duty cycle by factors between 2 – 4 will shorter the data taking periods significantly.

Also, the current high instantaneous rates due to the 100 kHz bunching by the resonant extraction are of concern. We require that this bunching be moderated to the extent possible. The requested instantaneous rates for pions and muons in the momentum range of 8 to 66 GeV/c and low energy electrons are most likely within present capabilities of the test beam.  However, it is likely that facility improvements for high energy electrons and low momentum pions, down to 1 GeV/c, will be required.

For most of the tests we request a beam spot of the order of 1 cm2. Some tests will require larger beam spots, e.g. when running with muons for calibration purposes. Here beam spots as large as technically feasible will be useful.

5.1 Electrons

Electron beams in the energy range of 2.5 GeV (if possible 1 GeV) to 25 GeV, momentum selected and/or tagged to ±1% sigma in this range, and Čerenkov tagged to high efficiency (better than 99 %), at rates of up to 1 kHz, with no more than a factor of 20 contamination by other particles in the beam are requested.   The material in the beamline must be minimized in order to reduce the radiation which spreads the energy spectrum of the electrons.  The momentum tail of the beam must be well understood.  It is expected that material reductions will be made with vacuum, helium bags, consideration of beam detector elements, etc.  An improvement of ratio of electrons to other particles may be required as tests progress. Either Čerenkov tagging to achieve a purity of 99.5 % or a modification of the beam operation to achieve this high purity will be required.

5.2 Muons

Muons, momentum selected for some tests, and with a spread of energies for other tests are required with fluxes up to 100 Hz/cm2 total over the beam, with no more than a factor of 20 contamination by other particles in the beam.  In the case that these are momentum selected, they must be Čerenkov tagged. Muons in the energy range between 2 and 20 GeV are required.

5.3 Pions

For some parts of the program the most stringent requirement is for low rates, a maximum 100 Hz/cm2, and in some cases, a maximum of 100 Hz total rate which is limited by the rate the data acquisition can handle.  Higher rates will be needed for some tests of the analog HCAL and the tail catcher.  At the early stage of the program (summer 2005), energies from 3 to 66 GeV are suitable.  The momentum must be tagged to ±1% sigma in the momentum range of 10 – 50 GeV and as precise as possible in other ranges. Čerenkov tagging to differentiate pions from kaons, protons, muons and electrons will be needed.  It is requested to bring the momenta of the pions down to 1 GeV/c by spring 2006 or six months into the program.   The low energy requirement of pions is driven by the average energies of hadrons in a typical jet in the linear collider environment.  Here, the requirements on momentum and Čerenkov tagging are as specified above.   It is also requested to select on charge of pions due to the significant differences observed in simulations between particles and anti-particles.

5.4 Protons

Finally, protons and anti-protons in the energy range of 3 to 66 GeV are requested. Again, for some of the program the rates need to be limited to 100 Hz/cm2, and in some cases to 100 Hz total. The momentum must be tagged to ±1% sigma in the momentum range of 10 – 50 GeV and as precise as possible in other ranges.  Protons of momentum up to 120 GeV are also requested. Čerenkov tagging to differentiate protons from kaons and pions/muons will be needed. It is also requested to select on charge of pions due to the significant differences observed in simulations between particles and anti-particles.

VI. Requirements: Floor space and infrastructure

6.1 Floor space

In order to allow for scans of the surface of the 1 m3 prototype hadronic section, a floor space of 5 m laterally and 3 m minimum longitudinally is requested.

6.2 Requirements on crane

A crane with a capacity of 20 tons will be needed to transport the prototype hadronic section into the test beam area. The weight of the prototype section including the scanning table is estimated to be between 10 and 15 tons.

6.3 Gas needs

Two versions of the hadronic calorimeter, RPCs and GEMs, require a mixture of gases for operation. The gas system will be provided by the detector groups, while the gases will be purchased via Fermilab through the experimental group’s operational expense account, unless the gas is readily available through the building infrastructure.

6.5 Cooling needs

Cooling water with a temperature close, but above the dew point, is requested. The maximum flow rate is to be specified in the near future.

6.6 Loading Areas

A crane accessible area with a large roll up door for a truck to back in for loading and unloading of prototype is necessary.

VII. Responsibilities by institutions: Non-Fermilab

Table 3 below list the primary (P) and technical (T) contacts of each detector technology.  It also specifies the primary contact for proposed test beam program, daily experimental contact for day-to-day operation and liaison to Fermilab.  The primary and technical contact persons from each technology will be responsible for setting up and operating their own test beam experiment.  Additional requests from these contact persons will be communicated to Fermilab through the daily experimental contact persons.  It is also envisioned, more specialized MOU’s will be provided by the groups carrying out the test if more details are needed beyond what is covered in this MOU.

Table 3 List of tasks and contact persons for each detector technology.  (P) stands for the primary contact and (T) stands for technical contact for the technology.  The names without the specifications are to act as both primary and technical contact.

| Responsibilities | Beam Test Contact | Institution |
| --- | --- | --- |
| Primary Physicist in Charge of Beam tests | J. C. Brient, J Yu | Ecole Polytechnique, University of Texas at Arlington |
| Daily Experimental Contact | J Repond, V. Zutshi | ANL, NIU/NICADD |
| Fermilab Liaison | E Ramberg | Fermilab |
| EM Calorimeter |
| Si-Tungsten | CALICE | J. C. Brient | LLR Ecole Polytechnique |
|  | US | D. Strom (P), M Breidenbach (T) | University of Oregon, SLAC |
| Scintillator-Tungsten | T Takeshita | Shinshu |
| Scintillator-Si-Tungsten | G. Wilson | University of Kansas |
| Scintillator-Si-Lead | P. Checchia | INFN Padova |
| Scintillator-Tungsten | U. Nauenberg (P), E. Erdos(T) | University of Colorado |
| Hadronic Calorimeter |
| Scintillator-Steel | F Sefkow, M Danilov | DESY, ITEP |
| RPC-Steel | CALICE-Russian | V Ammosov | IHEP |
|  | CALICE-US | J. Repond (P), L Xia (T) | ANL |
| GEM-Steel | A. White (P), J. Li (T) | University of Texas at Arlington |
| Muon –detector/Tail-catcher |
| Scintillator-Steel | V, Kobel, V. Zutshi | DESY, NIU/NICADD |
| RPC-Steel | Marcello Piccolo | Frascati |

VIII. Responsibilities by institutions: Fermilab

8.1 Accelerator Division

8.1.1 Improve the duty cycle (e.g. by increasing the spill length) to facilitate acquiring the data in a short and manageable time frame.

8.1.2 Commissioning of a beam line and delivery of beam of charge selected beam of pions at low momenta, start at 3 GeV/c for the first 6 months and down to 1 GeV/c after the initial 6 months of running.

8.1.3 Commissioning of an electron beam over as extensive a momentum range as possible, starting at 3 GeV/c to 25 GeV/c for the first 6 months and down to 1 GeV/c after the initial 6 months of running.

8.1.4 Provide a beam-line survey and the results.

8.1.5 Assist with modeling of beam-line optics, beam production, beam transport, momentum spread, material for multiple scattering, secondary particle production, and beam purities.

8.1.6 Provide beam diagnostics, beam profile, intensity, momentum bite, etc, information to the experiment via existing Accelerator network and monitoring system and technical assistance in merging them with experimental data.

8.2 Computing Division

8.2.1 Technical assistance in data acquisition, in particular with merging trigger information with calorimeter data, is needed.

8.2.2 Network: Establish and maintain wired and wireless internet connections: 16 wired connections in the MTBF office area, 10 in the counting house, and 10 in the experimental area at 100 Mbits/sec or better.  Wireless access points should be reachable from office, counting house and the experimental hall.  Two dedicated 1Gbit/sec connections between DAQ system and the data recorder are needed; one for primary recording and the other as the backup. The building network bandwidth should be 1 Gbit/sec or better for data transfer to off-site locations.

8.2.3 Data Storage: Data will be stored on tapes (technology to be determined in later dates) and RAID array disks, recorded by a DAQ computer in the office area.  Technical support to maintain the recording system and data copy and archival services are needed.  The tapes will be provided by the experimental group taking data at the given time.

8.2.4 Technical assistance with GEANT4 for construction and running of simulation programs are needed.

8.2.5 Repair services of electronics and trigger logic, as well as computing equipment.

8.3 Particle physics division

8.3.1 Minimization of material in electron beam-line.

8.3.2 Helium bags for beam transport.

8.3.3 Maintenance, commissioning and alignment of test-beam detectors, such as scintillation counters, Čerenkov counters, and Silicon tracking detectors.

8.3.4 Provision of beam-line related event data acquisition and assistance with integration of the dedicated detector data acquisition.  Assistance with integration of special triggers.

8.3.4 Maintenance of gas supply system

8.3.5 Office space for up to ten people at its maximum.

8.3.6 Provision of rigging and crane operations

IX. Access to data

All data collected at the test beam will be accessible to all members of the test beam effort via network transfer from the storage disk array and through tape copies.

X. Special Considerations

10.1	The responsibilities of the primary physicists in charge of the test beam program and the procedures to be followed by experimenters are found in the Fermilab publication "Procedures for Experimenters" (PFX). The physicists participating in the test beam program agree to those responsibilities and to follow the described procedures.

10.2	To carry out the experiment a number of Environmental, Safety and Health (ES&H) reviews are necessary. This includes creating a Partial Operational Readiness Clearance document in conjunction with the standing Particle Physics Division committee. The physicists in charge of the test beam program will follow those procedures in a timely manner, as well as any other requirements put forth by the division’s safety officer.

10.3	The physicists in charge of the test beam program will ensure that at least one person is present at the Meson Test Beam Facility whenever beam is delivered and that this person is knowledgeable about the experiment’s hazards.

10.4	All regulations concerning radioactive sources will be followed.  No radioactive sources will be carried onto the site or moved without the approval of the Fermilab ES&H section.

10.5	All items in the Fermilab Policy on Computing will be followed by the experimenters.

10.6	The physicists in charge of the test beam program will undertake to ensure that no PREP or computing equipment be transferred from the experiment to another use except with the approval of and through the mechanism provided by the Computing Division management. They also undertake to ensure that no modifications of PREP equipment take place without the knowledge and consent of the Computing Division management.

10.7	The test beam group will be responsible for maintaining and repairing both the electronics and the computing hardware supplied by them for the experiment. Any items for which the experiment requests that Fermilab performs maintenance and repair should appear explicitly in this agreement.

10.8	At the completion of the experiment:

10.8.1	The physicists in charge of the test beam program are responsible for the return of all PREP equipment, computing equipment and non-PREP data acquisition electronics. If the return is not completed after a period of one year after the end of running, the physicists in charge will be required to furnish, in writing, an explanation for any non-return.

10.8.2	The experimenters agree to remove their experimental equipment as the Laboratory requests them to. They agree to remove it expeditiously and in compliance with all ES&H requirements, including those related to transportation. All the expenses and personnel for the removal will be borne by the experimenters.

10.8.3	The experimenters will assist the Fermilab Divisions and Sections with the disposition of any articles left in the offices they occupied, including computer printout and magnetic tapes.

10.8.4	An experimenter will report on the test beam effort at the Fermilab All Experimenters Meeting.

Bibliography

- C. Altunbas et al., Nucl. Inst. Meth. A490, 177 (2002)

- S. Agostinelli et al. (GEANT4 Collaboration) Nucl. Instrum. Methods A506 (2003) 250, http://geant4.web.cern.ch/geant4/ and references therein for the various models implemented.

- A. Fasso, A. Ferrari, J. Ranft and P. R. Sala, “FLUKA: present status and future developments,” Proc. Of the 4th International Conference on Calorimetry in High Energy Physics, Eds. A. Menzione and A. Scribano, World Scientific, p493 (1993); A. Fasso et al., “The Physics Models of FLUKA: Status and Recent Developments,” Talk given at 2003 Conference for Computing in High-Energy and Nuclear Physics (CHEP 03), La Jolla, California, hep-ph/0306267 (2003)

- H.J. Klein and J. Zoll. PATCHY Reference Manual, Program Library L400. CERN (1988).

- T.A. Gabriel, J.D. Amburgey, B.L. Bishop, “CALOR: A Monte Carlo Program Package for The Design and Analysis of Calorimeter Systems,” Oak Ridge National Laboratory Technical Memo, ORNL/TM-5619, Unpublished (1977)

- G. Mavromanolakis & D. Ward, “Comparisons of Hadronic Shower Pacakges,” e-Print Archive: physics/0409040, To appear in the proceedings of International Conference on Linear Colliders (LCWS 04), Paris, France, 19-24 Apr 2004.

- Resistive Plate Chamber references

- R. Bouclier, et al., “The Gas Electron Multiplier (GEM),” IEEE Trans. Nucl. Sci. NS-44, 646 (1997);  F. Sauli “GEM: A new concept for electron amplification in gas detectors,” Nucl. Inst. Meth., A386, 531 (1997)

- L.Rolandi and R.Klanner, “Recommendations of the 57th Meeting of the PRC at DESY,” http://www.desy.de/f/prc/minutes/prc_57_Directorate_recommendations.pdf (2004)

- CALICE Collaboration: http://polywww.in2p3.fr/flc/calice.html

- P. Buzhan et al., “An Advanced Study of Silicon Photomultiplier,“ ICFA Instrum. Bull. 23:28-41 (2001); P. Buzhan et al., “Silicon Photomultiplier And Its Possible Applications,” Nucl.Instrum.Meth.A504, 48 (2003)

- M. Bettini et al., “Silicon Pad Detectors for LCCAL: Characterization and Test Beam Results,” LC-DET-2003-101, Unpublished (2003)

- V. Rusinov et al., CALICE Collaboration, “The Scintillator Tile Hadronic Calorimeter Prototype,” Presented at the 9th Topical Seminar on Innovative Particle and Radiation Detectors, May (2004)

- V. Korbel, CALICE Collaboration,“The Tile-HCAL Physics Prototype,” ECFA Study for Physics and Detectors for a Linear Collider, Montepellier, France, Nov. (2003)

- D. Ward, CALICE Collaboration, “CALICE ECAL + HCALs TB plans,” ECFA Linear Collider Workshop, Durham, UK, Sept. (2004)

XI. Signatures

________________________________	/      / 2004

Jaehoon Yu, University of Texas at Arlington

________________________________	/      / 2004

Jean-Claude Brient, CALICE Spokesperson

(LLR Ecole Polytechnique)

________________________________	/      / 2004

José Repond, Argonne National Laboratory

______________________________________	/      / 2004

James Strait, Particle Physics Division

______________________________________	/      / 2004

Roger Dixon, Accelerator Division

______________________________________	/      / 2004

Robert Tschirhart, Computing Division

______________________________________	/      / 2004

William Griffing, ES&H Section

_______________________________________      /      /2004

Hugh Montgomery, Associate Director, Fermilab

_______________________________________      /      /2004

Steven Holmes, Associate Director, Fermilab

# Text boxes

Figure 2 A schematic diagram of CALICE HCAL movable stand.  It can hold the entire calorimeter prototype modules, both ECAL and HCAL, and position the setup any direction in all three dimensions.