FLC_PHY3 Front end chip

DATASHEET

# Table of content

1.	Table of content	2

2.	Table of figures	3

3.	General description	4

4.	One channel description	5

4.1.	Charge preamplifier	5

4.2.	Shapers	8

4.3.	Track and hold	8

4.4.	Output buffer	10

4.5.	Multiplexer description	10

5.	Pin definition	12

6.	Characteristics & measurement	14

6.1.	DC Levels	14

6.2.	Transient	15

6.2.1.	Output signal shape	15

6.2.2.	Output signal dispersion	15

6.2.3.	Preamplifier gain measurement	16

6.3.	Linearity	17

6.3.1.	Linearity measurement – Cf=3pF	18

6.3.2.	Linearity measurement – Cf=1.6pF	19

6.3.3.	Linearity measurement – Cf=0.8pF	20

6.3.4.	Linearity measurement – Cf=0.4pF	21

6.3.5.	Linearity measurement – Cf=0.2pF	22

6.4.	Crosstalk	23

6.5.	Noise	26

6.5.1.	Gain 1	26

6.5.2.	Gain 10	27

6.5.3.	Charge Preamplifier	29

6.6.	Pedestal dispersion	30

# Table of figures

Figure 1 General block schema of FLC_PHY3	4

Figure 2 - Block schema of one channel	5

Figure 3 - Schema of charge preamplifier	6

Figure 4 - preamplifier resistor feedback	8

Figure 5 - CRRC shaper schematic	8

Figure 6- Block diagram of the channel N track and hold	9

Figure 7 - Block diagram of the shift register	11

Figure 8 - Chronogram of the multiplexed readout	11

Figure 9 - Transient of gain 1 and gain 10 shapers output	15

Figure 10 - Transient of gain 1 shaper output vs feedback capacitance	15

Figure 11 – Preamplifier measured feedback capacitance vs theoretic capacitance	17

Figure 12 - Linearity - Cf=3pF	18

Figure 13 - Linearity - Cf=1.6pF	19

Figure 14 - Linearity - Cf=0.8pF	20

Figure 15 - Linearity - Cf=0.4pF	21

Figure 16 - Linearity - Cf=0.2pF	22

Figure 17 - Output noise versus input capacitance - gain 1	26

Figure 18 - Equivalent input noise charge versus input capacitance - gain 1	27

Figure 19 - Output noise versus input capacitance - gain 10	28

Figure 20 - Equivalent input noise charge versus input capacitance – Gain 10	28

Figure 21 - FLC_PHY3 preamp ENC (e-) vs Tp (s)	29

Figure 22 - Pedestal measurement on Gain 1 output	31

Figure 23 - Pedestal measurement on gain 10 output	31

Table 1- Compensation capacitance values	7

Table 2 - Gain versus feedback capacitance switch configuration	7

Table 3 - follower switch SW description	9

Table 4 - measured vs simulated DC levels	14

Table 5 - Gain and peaking time dispersion	16

Table 6 - Theoretic vs measured preamplifier gain	16

Table 7 - Characterization Cf=3pF	18

Table 8 - Characterization Cf=1.6pF	19

Table 9 - Characterization Cf=0.8pF	20

Table 10 - Characterization Cf=0.4pF	21

Table 11 - Characterization Cf=0.2pF	22

Table 12 – Gain 1 Crosstalk measurement	24

Table 13 – Gain 10 Crosstalk measurement	25

Table 14 - Pedestal measurement	30

Equation 1 - Shaper transfer function	8

# General description

The FLC_PHY3 Front-end chip is an 18-channel charge input front end circuit. It provides a shaped signal proportional to the input charge.

Figure 1 General block schema of FLC_PHY3

Each channel is made of a variable-gain charge preamplifier followed by two parallel shaping filter of different gain (1 and 10) using a CRRC structure. Each of these shaper are followed by a track & hold device driving a single multiplexed output.

The bias of each stage is common for every channel.

# One channel description

Figure 2 - Block schema of one channel

Figure 2 shows a simplified block schema of one channel. The first stage is made of a multi-gain charge preamplifier. Four switchable feedback capacitance allow to tune the gain within 16 gains. After the preamplifier, the circuit is doubled to optimise dynamic range. Two shapers with different gains (1 and 10) allows to reduce noise. Hence there is two shaped signal available. Choosing one or the other may depend on the magnitude of the signal. A track and hold device allowing multiplexing follows each of the shaper.

Each functional block will be described in detail below.

## Charge preamplifier

Figure 3 - Schema of charge preamplifier

The first stage of that preamplifier is a common source transistor biased by a current source made of two NMOS transistor connected as a current mirror.

It is recommended to let flow at least 500µA in the input PMOS to reduce series noise by increasing the PMOS gm. That means Vbiasi_pa should be connected to the Vdd with a resistor smaller than 10kΩ (typ. 6.7kΩ for Ids=500µA or 3.3 kΩ for Ids=1mA).A compromise have to be done at this point by the designer between consumption and noise. Vbiasi_pa is the current source of the input PMOS and the bipolar cascode. The current flowing in the input PMOS can be calculated by subtracting the cascode current (provided by the Vbiasm_pa current source) to the input current source.

The second stage is a common base bipolar transistor (NPN) in a cascode structure. The Vb pin allows to tune the input PMOS Vds. The Vbiasm_pa bias the bipolar transistor with a DC current.

After the second stage are the compensation capacitors that  allows to slow the preamplifier down in case of oscillation, if the impedance on the input is not enough capacitive. The value of the compensation capacitance are given in Table 1.

| Capacitance | Value |
| --- | --- |
| Switch 1 | 4pF |
| Switch 2 | 2pF |
| Switch 3 | 1pF |

Table 1- Compensation capacitance values

The third stage is a follower (common drain PMOS) biased by a current source (Vbiaso_pa).

The feedback capacitor is tuneable. 4 switched capacitors allows to choose within 16 gain. The different gain are listed in Table 2.

| Switch configuration | Feedback Capacitance | Gain |
| --- | --- | --- |
| Capa SW0=1.6pF | Capa SW1=0.8pF | Capa SW2=0.4pF | Capa SW3=0.2pF |  |  |
| OFF | OFF | OFF | OFF | 0pF | N/A |
| OFF | OFF | OFF | ON | 0.2pF | 5V/pC |
| OFF | OFF | ON | OFF | 0.4pF | 2.5V/pC |
| OFF | OFF | ON | ON | 0.6pF | 1.67V/pC |
| OFF | ON | OFF | OFF | 0.8pF | 1.25V/pC |
| OFF | ON | OFF | ON | 1pF | 1V/pC |
| OFF | ON | ON | OFF | 1.2pF | 830mV/pC |
| OFF | ON | ON | ON | 1.4pF | 714mV/pC |
| ON | OFF | OFF | OFF | 1.6pF | 625mV/pC |
| ON | OFF | OFF | ON | 1.8pF | 555mV/pC |
| ON | OFF | ON | OFF | 2pF | 500mV/pC |
| ON | OFF | ON | ON | 2.2pF | 455mV/pC |
| ON | ON | OFF | OFF | 2.4pF | 416mV/pC |
| ON | ON | OFF | ON | 2.6pF | 385mV/pC |
| ON | ON | ON | OFF | 2.8pF | 357mV/pC |
| ON | ON | ON | ON | 3pF | 333mV/pC |

Table 2 - Gain versus feedback capacitance switch configuration

The resistor feedback is made of two unbalanced current mirror and a resistor (Figure 3).That makes the resistor virtually bigger.

The output transistor of the mirror is 25 times bigger than the input one, that means the current in the input line is 25 times lower. Considering there is two stage, the input current is 625 smaller than the output one which is flowing in the feedback resistor. The resistor seen at the input of the preamp is then virtually 625 bigger than its real value (36kΩ*625=22.5MΩ, Figure 4).

Figure 4 - preamplifier resistor feedback

## Shapers

Shapers are CRRC active filters that use operational amplifiers (Figure 5). The differential input of an operational amplifier allows to reduce the pedestal dispersion of shapers due to a DC loop feedback.

The DC reference allows to tune the output DC level. The transfer function of shapers is given on Equation 1. A decoupling capacitor have been added to reduce the shaper noise that was abnormally high in FLC_PHY2 version.

Figure 5 - CRRC shaper schematic

Equation 1 - Shaper transfer function

## Track and hold

The track and hold allows to memorize an analogue value in a capacitance using a CMOS switch driven by the hold signal (pin H). That hold signal have to be synchronized with the peaking time of the shaper to ensure a maximum dynamic range and offset swing. The analogue value can then be red through the read CMOS switch. A follower forbids the charge of the capacitance to go away through the readout electronic. The value is then conserved during the reading. It is possible to choose between two different follower architecture. The first one is a simple common collector as on FLC_PHY1 chip. The second one use a differential structure (Widlar) to optimise pedestal dispersion. The pin SW permits to choose between common collector or Widlar structure (Table 3).

| SW=1(Vdd) | SW=0(Vss) |
| --- | --- |
| Common collector | Widlar structure |

Table 3 - follower switch SW description

The read switch is driven by a D latch cascaded as a shift register. That system allows to read sequentially the analogue value of the 18 channels of the selected gain with the multiplexed output.. A block diagram of the track and hold is shown on Figure 6.

Figure 6- Block diagram of the channel N track and hold

## Output buffer

The output buffer is made of an OTA with a unit feedback on the negative input. The bias_buf pin is to bias the input differential peer of the OTA. 100 µA DC current is needed to bias that first stage. A 47 kΩ resistor to Vdd allows to obtain that current.

## Multiplexer description

There has been major modifications of the multiplexer between FLC_PHY2 and FLC_PHY3.

The two outputs of FLC_PHY2 (G1 and G10) are now mixed up in a single output (OUTPUT G1/G10). The choice of the gain can be made with an asynchronous gain selection switch.

The two shift registers (one for gain 1, one for gain 10) have the same digital control. That is to say they both will have the same behaviour to the same stimuli. In other words the two shift registers will always be in the same state (Figure 7).

In normal use, that involves the same channel will be active for gain 1 and gain 10 at a given time (see chronogram in Figure 8).

According to that symetry, the choice of the gain at the output will be done for a given channel. For example if the channel 2 is active for gain 1, channel 2 is active for gain 10 too. The choice of the gain will then be done for channel 2.

To keep the pin to pin compatibility with both FLC_PHY1 and FLC_PHY2, there is only one shift register output even if there is now two shift register. The Gain one shift register has been chosen to have an output. There is therefore now output for gain 10 shift register.

Figure 7 - Block diagram of the shift register

Figure 8 - Chronogram of the multiplexed readout

# Pin definition

| Pin number | Pin name | definition |
| --- | --- | --- |
| 64,1-8,10-18 | In 0 – in 17 | 18 charge inputs |
| 9,22,23,28, 41,51,60 | Vss | Low supply (substrate bias) |
| 19,26,31, 32,40,42,63 | Vdd | High supply |
| 20,21,34,35 | SW1,SW2,SW3, SW4 | CMOS preamp feedback capacitor switch SW0 : 1.6 pF SW1 : 0.8 pF SW2 : 0.4 pF SW3 : 0.2 pF |
| 37 – 39 | SW_C1, SW_C2, SW_C3 | CMOS preamp compensation capacitor switch SW_C1 : 4pF SW_C2 : 2pF SW_C3 : 1pF |
| 47 | SW | Widlar or common collector buffer switch |
| 50 | Rst_R | CMOS shift registers reset |
| 53 | Ck_R | CMOS shift registers clock |
| 54 | H | CMOS Hold command |
| 52 | D_R | CMOS Gain 1 and Gain 10 shift registers input |
| 25 | Q_R | CMOS Gain 1 shift register output |
| 27 | OUT_g1 | Gain 1 multiplexed output |
| 43 | SW_gain | Gain 1 – gain 10 selection switch |
| 24 | Vref_sh1 | Gain 1 shaper voltage reference for differential |
| 29 | Vref1_sh10 | Gain 10 shaper voltage reference for differential |
| 30 | Vref2_sh10 | Gain 10 shaper voltage reference for anti-saturation |
| 62 | Ibi_pa | Preamplifier input stage current bias |
| 58 | Ibm_pa | Preamplifier middle-stage current bias |
| 57 | Ibm_pa | Preamplifier out-stage current bias |
| 61 | Vb_pa+Vbf | Base cascode transistor voltage bias and feedback resistor cascode transistor voltage bias |
| 59 | If_pa | Feedback preamplifier leakage current bias (should be around 100nA) |
| 56 | Ibi_sh1 | Current bias of gain 1 shaper input stage |
| 55 | Ibo_sh1 | Current bias of gain 1 shaper output stage |
| 49 | Ibi_sh10 | Current bias of gain 10 shaper input stage |
| 48 | Ibo_sh10 | Current bias of gain 10 shaper output stage |
| 46 | Ibi_wid | Current bias of widlar buffer input stage |
| 44 | Ibo_wid | Current bias of widlar buffer output stage |
| 45 | Ib_cc | Current bias of common collector buffer |
| 33 | Ib_OTA | Current bias of OTA output buffer |
| 36 | Out_preamp | Channel 17 preamp output |

# Characteristics & measurement

## DC Levels

Following DC levels have been measured and simulated on FLC_PHY3 chip :

| Block | Bias name | Simulation result | Measurement | Current yield |
| --- | --- | --- | --- | --- |
| Preamplifier | Ibi_pa | -3.3V | -3.2V | 1mA |
|  | Ibm_pa | -1.37V | -1.4V | 70uA |
|  | Ibo_pa | -1.28V | -1.3V | 100uA |
|  | If_pa | -0.7V | -0.7V | 100nA |
|  | Vb_pa | -3.5V | -3.5V | None – voltage ref. |
| Shaper 1 | Ibi_sh1 | -3.7V | -3.7V | 50uA |
|  | Ibo_sh1 | -3.7V | -3.7V | 50uA |
|  | Vref_sh1 | -3.8V | -3.7V | None – voltage ref. |
| Shaper 10 | Ibi_sh10 | -3.7V | -3.7V | 50uA |
|  | Ibo_sh10 | -3.7V | -3.7V | 50uA |
|  | Vref1_sh10 | -3.8V | -3.7V | None – voltage ref. |
|  | Vref2_sh10 | -2V | -2V | None – voltage ref. |
| Track&hold | Ib_cc | -1.4V | -1.5V | 50uA |
|  | Ibi_wid | -3.7V | -3.7V | 50uA |
|  | Ibo_wid | -3.7V | -3.7V | 50uA |
| OTA | Ib_ota | -3.7V | -3.9V | 50uA |

Table 4 - measured vs simulated DC levels

Consumption of the whole chip is 150mW. That makes a 8.2mW dissipation per channel. It is easy to reduce that consumption by reducing input transistor bias current depending on noise yield and input capacitance. Setting a 200uA input current makes the consumption fall down to 4mW per channel.

## Transient

### Output signal shape

The output signal shape has been monitored to check the response of the CRRC filter (Figure 9).

Figure 9 - Transient of gain 1 and gain 10 shapers output

The same measurement has been made with several preamp feedback capacitance (Figure 10). The gain variation is qualitatively validated.

Figure 10 - Transient of gain 1 shaper output vs feedback capacitance

### Output signal dispersion

The output signal has been measured on all channels. Statistic calculation has been done to estimate the peaking time and magnitude dispersion. Results are reported in Table 5.

|  | Gain 1 | Gain 10 |
| --- | --- | --- |
| Channel | Mag. (mV) | Tp (ns) | Mag. (mV) | Tp (ns) |
| 1 | 35 | 191 | 320 | 173 |
| 2 | 35,1 | 192 | 314 | 174 |
| 3 | 35,1 | 189 | 316 | 172 |
| 4 | 35,1 | 189 | 322 | 177 |
| 5 | 33,9 | 188 | 307 | 175 |
| 6 | 33,2 | 187 | 302 | 176 |
| 7 | 34,5 | 186 | 308 | 172 |
| 8 | 34,6 | 190 | 312 | 175 |
| 9 | 33,9 | 188 | 307 | 176 |
| 10 | 35,4 | 186 | 319 | 174 |
| 11 | 35,5 | 189 | 319 | 171 |
| 12 | 33 | 186 | 297 | 171 |
| 13 | 33,9 | 187 | 313 | 174 |
| 14 | 35,2 | 188 | 320 | 171 |
| 15 | 35 | 191 | 312 | 169 |
| 16 | 34 | 189 | 312 | 174 |
| 17 | 37,3 | 190 | 341 | 172 |
| 18 | 35,2 | 190 | 316 | 174 |
| mean. | 34,717 | 188,667 | 314,278 | 173,333 |
| Std dev. | 0,990 | 1,815 | 9,398 | 2,114 |
| std dev/mean | 2,85% | 0,96% | 2,99% | 1,22% |

Table 5 - Gain and peaking time dispersion

### Preamplifier gain measurement

Preamplifier gains has been measured depending on feedback capacitance with an input charge of 100fC. Results are presented in Table 6.

| Theoretic gain | theoretic Cf | Vout preamp | Meas. Gain | Meas. Cf |
| --- | --- | --- | --- | --- |
| - | 0 | - | - | - |
| 5 | 0,2 | 0,4934 | 4,934 | 0,2027 |
| 2,5 | 0,4 | 0,2658 | 2,658 | 0,3762 |
| 1,67 | 0,6 | 0,1822 | 1,822 | 0,5488 |
| 1,25 | 0,8 | 0,13898 | 1,3898 | 0,7195 |
| 1 | 1 | 0,11052 | 1,1052 | 0,9048 |
| 0,83 | 1,2 | 0,09334 | 0,9334 | 1,0714 |
| 0,71 | 1,4 | 0,07936 | 0,7936 | 1,2601 |
| 0,625 | 1,6 | 0,06784 | 0,6784 | 1,4741 |
| 0,56 | 1,8 | 0,06034 | 0,6034 | 1,6573 |
| 0,5 | 2 | 0,05526 | 0,5526 | 1,8096 |
| 0,45 | 2,2 | 0,0502 | 0,502 | 1,9920 |
| 0,42 | 2,4 | 0,04628 | 0,4628 | 2,1608 |
| 0,38 | 2,6 | 0,0428 | 0,428 | 2,3364 |
| 0,36 | 2,8 | 0,03966 | 0,3966 | 2,5214 |
| 0,33 | 3 | 0,03698 | 0,3698 | 2,7042 |
| Unit : V/pC | Unit : pF | Unit : V | Unit : V/pC | Unit : pF |

Table 6 - Theoretic vs measured preamplifier gain

Results presented in Table 6 allow to compare measured feedback capacitance with theoretic capacitance. That comparison is done in Figure 11.

Figure 11 – Preamplifier measured feedback capacitance vs theoretic capacitance

Measured capacitance are smaller than expected (-10.32%). Parasitic capacitance between output and input is around 14fF.

## Linearity

Linearity has been measured on both shaper gain 1 and gain 10. Several preamp gain configuration has been tested. FLC_PHY3 provides a 135 factor between highest and lowest channel gain. Considering  a 6.72 fC MIP, Full range is from 6.6 MIP (highest gain) to 900 MIP (lowest gain). Linearity is around a few per thousand.

Max input and output signal, linearity measurement and gain calculation are detailed for a few preamp gain below.

### Linearity measurement – Cf=3pF

#### Switch configuration

| Switch 0 | Switch 1 | Switch 2 | Switch 3 |
| --- | --- | --- | --- |
| ON | ON | ON | ON |

#### Measurement results

Figure 12 - Linearity - Cf=3pF

| Shaper gain | 1 | 10 |
| --- | --- | --- |
| Qin max | 6.04 pC | 0.605 pC |
| Vout max | 1.26 V (over 50 () | 1.09V (over 50 () |
| Gain | 211 mV/pC | 1820 mV/pC |
| Feedback cap | 2.36 pF | 2.74pF |
| Non-linearity | 1.6‰ | 3.7‰ |

Table 7 - Characterization Cf=3pF

### Linearity measurement – Cf=1.6pF

#### Switch configuration

| Switch 0 | Switch 1 | Switch 2 | Switch 3 |
| --- | --- | --- | --- |
| ON | OFF | OFF | OFF |

#### Measurement results

Figure 13 - Linearity - Cf=1.6pF

| Shaper gain | 1 | 10 |
| --- | --- | --- |
| Qin max | 3.27 pC | 0.33 pC |
| Vout max | 1.27 V (over 50 () | 1.12 V (over 50 () |
| Gain | 391 mV/pC | 3.44 V/pC |
| Feedback cap | 1.27 pF | 1.45 pF |
| Non-linearity | 3.2‰ | 3.6‰ |

Table 8 - Characterization Cf=1.6pF

### Linearity measurement – Cf=0.8pF

#### Switch configuration

| Switch 0 | Switch 1 | Switch 2 | Switch 3 |
| --- | --- | --- | --- |
| OFF | ON | OFF | OFF |

#### Measurement results

Figure 14 - Linearity - Cf=0.8pF

| Shaper gain | 1 | 10 |
| --- | --- | --- |
| Qin max | 1.65 pC | 0.187 pC |
| Vout max | 1.28 V (over 50 () | 1.26 V (over 50 () |
| Gain | 778 mV/pC | 6.83 V/pC |
| Feedback cap | 0.64 pF | 0.73 pF |
| Non-linearity | 3.1‰ | 7.9‰ |

Table 9 - Characterization Cf=0.8pF

### Linearity measurement – Cf=0.4pF

#### Switch configuration

| Switch 0 | Switch 1 | Switch 2 | Switch 3 |
| --- | --- | --- | --- |
| OFF | OFF | ON | OFF |

#### Measurement results

Figure 15 - Linearity - Cf=0.4pF

| Gain shaper | 1 | 10 |
| --- | --- | --- |
| Qin max | 0.817 pC | 89.9 fC |
| Vout max | 1.24 V (over 50 () | 1.23 V (over 50 () |
| Gain | 1.53 V/pC | 14 V/pC |
| Feedback cap | 0.33 pF | 0.36 pF |
| Non-linearity | 2.4‰ | 8.1‰ |

Table 10 - Characterization Cf=0.4pF

### Linearity measurement – Cf=0.2pF

#### Switch configuration

| Switch 0 | Switch 1 | Switch 2 | Switch 3 |
| --- | --- | --- | --- |
| OFF | OFF | OFF | ON |

#### Measurement results

Figure 16 - Linearity - Cf=0.2pF

| Shaper gain | 1 | 10 |
| --- | --- | --- |
| Qin max | 0.41 pC | 44.2 fC |
| Vout max | 1.19 V (over 50 () | 1.24 V (over 50 () |
| Gain | 2.96 V/pC | 28.6 V/pC |
| Feedback cap | 0.17 pF | 0.18 pF |
| Non-linearity | 3.4‰ | 16‰ |

Table 11 - Characterization Cf=0.2pF

## Crosstalk

Crosstalk has been measured for Gain 1 and gain 10. Average crosstalk is below 1‰ in the 4 nearest channel around hit channel. A 3.4pC charge is injected in channel 4 for Gain 1 crosstalk measurement. A 0.34pC charge is injected in channel 4 for gain 10 crosstalk measurement.

| Channel 2 |  | Signal magnitude @ peaking time : 929μV (0.75‰ of signal) |
| --- | --- | --- |
| Channel 3 |  | Signal magnitude @ peaking time : 1.884mV (1.52‰ of signal) |
| Channel 4 |  | HIT CHANNEL Injected charge : 5pC Signal magnitude @ peaking time : 1238.3mV (100% of signal) |
| Channel 5 |  | Signal magnitude @ peaking time : 1.071mV (0. 86‰ of signal) |
| Channel 6 |  | Signal magnitude @ peaking time : 676μV (0.55‰ of signal) |

Table 12 – Gain 1 Crosstalk measurement

| Channel 2 |  | Signal magnitude @ peaking time : 700μV (0.639‰ of signal) |
| --- | --- | --- |
| Channel 3 |  | Signal magnitude @ peaking time : 910μV (0.831‰ of signal) |
| Channel 4 |  | HIT CHANNEL Injected charge : 5pC Signal magnitude @ peaking time : 1094mV (100% of signal) |
| Channel 5 |  | Signal magnitude @ peaking time : 914μV (0. 84‰ of signal) |
| Channel 6 |  | Signal magnitude @ peaking time : 825μV (0.75‰ of signal) |

Table 13 – Gain 10 Crosstalk measurement

## Noise

Output noise and ENC (Equivalent noise charge) have been measured on a whole line with gain 1 and gain 10. A sweep of the input capacitance has been made. These noise measurements have been made with the § 6.1 DC levels.

### Gain 1

Results of gain 1 are provided in Figure 17 and Figure 18.

Figure 17 - Output noise versus input capacitance - gain 1

Figure 18 - Equivalent input noise charge versus input capacitance - gain 1

These results are better than FLC_PHY2 measurement due to the decoupling capacitance of the shaper DC reference. ENC is 1500 e- better than FLC_PHY2 (dotted line in Figure 18).

### Gain 10

Results of gain 1 are provided in Figure 19 and Figure 20.

Figure 19 - Output noise versus input capacitance - gain 10

Figure 20 - Equivalent input noise charge versus input capacitance – Gain 10

### Charge Preamplifier

FLC_PHY3 provide a direct preamp output on channel 18. That allows to measure preamp noise precisely. ENC curves have been drawn to find the serial noise of the preamplifier ( Parallel noise is neglected).

Figure 21 - FLC_PHY3 preamp ENC (e-) vs Tp (s)

A fit of these curves gives a serial noise of  . Expectation was .

There is an improvement here. FLC_PHY2 has a  serial noise.

## Pedestal dispersion

Pedestal dispersion has been measured on both gain using both track and hold follower (Widlar and common collector). Measurement and stats are in Table 14. Figure 22 and Figure 23 show graphically the pedestal measurement on gain 1 and gain 10 respectively.

|  | Pedestal measurement (V) |
| --- | --- |
|  | Gain 1 | Gain 10 |
| Channel | Com. Col | Widlar | Com. Col. | Wid. |
| 1 | -2,7839 | -3,7017 | -2,8082 | -3,735 |
| 2 | -2,7872 | -3,6895 | -2,8163 | -3,731 |
| 3 | -2,7899 | -3,7042 | -2,7985 | -3,7316 |
| 4 | -2,7706 | -3,7023 | -2,8381 | -3,7252 |
| 5 | -2,7829 | -3,7032 | -2,8034 | -3,7237 |
| 6 | -2,781 | -3,6934 | -2,8012 | -3,7296 |
| 7 | -2,7679 | -3,7037 | -2,8048 | -3,7338 |
| 8 | -2,7688 | -3,7005 | -2,8146 | -3,7207 |
| 9 | -2,7745 | -3,7046 | -2,8241 | -3,748 |
| 10 | -2,7839 | -3,7036 | -2,7982 | -3,7238 |
| 11 | -2,7868 | -3,6955 | -2,8101 | -3,7355 |
| 12 | -2,761 | -3,7093 | -2,8131 | -3,7443 |
| 13 | -2,7913 | -3,7044 | -2,8227 | -3,7327 |
| 14 | -2,787 | -3,7067 | -2,8085 | -3,7215 |
| 15 | -2,7805 | -3,6953 | -2,8113 | -3,741 |
| 16 | -2,7846 | -3,7036 | -2,8357 | -3,7465 |
| 17 | -2,7906 | -3,7003 | -2,793 | -3,7227 |
| 18 | -2,7825 | -3,7005 | -2,8057 | -3,7237 |
| Min. value (V) | -2,7913 | -3,7093 | -2,8381 | -3,748 |
| Max. Value (V) | -2,761 | -3,6895 | -2,793 | -3,7207 |
| Max -Min (mV) | 30,3 | 19,8 | 45,1 | 27,3 |
| Mean (V) | -2,7808 | -3,7012 | -2,8115 | -3,7317 |
| Std dev. (mV) | 8,72 | 4,95 | 12,30 | 8,76 |

Table 14 - Pedestal measurement

Figure 22 - Pedestal measurement on Gain 1 output

Figure 23 - Pedestal measurement on gain 10 output

# Text boxes

Buffer

OUT

Channel 0

Shaper

G=1

T&Hold

IN 0

Shaper

G=10

T&Hold

4

Gain select

Channel 1

Shaper

G=1

T&Hold

IN 1

Shaper

G=10

T&Hold

Channel 17

preamp

Shaper

G=1

T&Hold

IN 17

Shaper

G=10

T&Hold

MUX ctrl

preamp

preamp

Amp

OPA

OPA

MUX out Gain=1

## MUX out Gain=10

Input

25

25

1

1

0.2pF

0.4pF

0.8pF

1.6pF

1pF

2pF

4pF

Preamp out

Preamp in

I

I/25

I/625

25

25

1

1

36kΩ

C1

R1

C2

R2

-

+

IN

DC ref

OUT

Reset

CMOS switch

CMOS switch

To Multiplexed output buffer

D latch

Clock

Reset

D

Q

From shaper

Hold

Clock

To D of channel N+1

From Q of channel N-1

Widlar

follower

IN

OUT

Follower selec. switch

CLK

##### D

RST

SRIN

G1

READ0

G1

READ1

G1

READ2

G1

READ16

G1

READ17

##### D

##### D

##### D

##### D

CLK

##### D

RST

SROUT

##### D

##### D

##### D

##### D

G10

READ0

G10

READ1

G10

READ2

G10

READ16

G10

READ17

RST

CLK

SRIN

Gain_SW

SROUT

G1

Ch.0

G1

Ch.1

G10

Ch.2

G10

Ch.3

Hold

0

1

2

3

16

17

18

OUT

G10

Ch.16

G1

Ch.17

Ibm_pa

Rst_R

Ibo_sh10

SW

Ibi_wid

Ib_cc

Ibo_wid

Vddd

SW_gain

Vdd_ota+diode

SW_C2

SW_C3

Vss_ota

Out_preamp

SW3

Ib_ota

SW2

SW_C1

Vdd_pa

In 0

Ibi_pa

Vb_pa + Vbf

Vss_pa

If_pa

Ibo_pa

Ibo_sh1

Ibi_sh1

H

D_R

Vss_setH

Ibi_sh10

In 16

Ck_R

In 1

In 2

In 3

In 4

In 5

In 6

In 7

In 8

Vss

In 9

In 10

In 11

In 12

In 15

In 14

In 13

SW0

In 17

Vdd_pa

SW1

Vss_pa

Vss_sh1

Vref_sh1

Q_R

Vdd_sh1

OUT_g1

Vss_sh10

Vref1_sh10

Vdd_sh10

Vref2_sh10

Vdd_setH

1

2

3

4

5

6

7

8

10

9

11

12

13

14

15

16

17

18

19

20

21

24

22

23

31

30

29

28

27

26

25

40

39

38

32

37

36

35

34

33

47

46

45

44

43

42

41

51

50

49

48

56

57

58

59

60

61

62

63

64

55

54

53

52

FLC_PHY3

TQFP 64 package