Problem Report 	Report Number:  5

Project Name:  TeraPixel APS for CALICE    v1.1

Item:  Configuration Registers: Power droop in buffer supplies

Problem

Were reporting many errors and not holding the correct data Problem due to different power domains and high loading of “slow” clock drivers

Originator (Sign/Date) JC

Project Manager (Sign/Date)

Remedial Action

Fixed by driving one of the power domains at 1.6v (previously 1.8v) Implemented using the power module developed for TPAC1.0 with updated resistor values and driving VDD1V8sram through J7 Proved, reliable fix provided 2% tolerance on resistors on power module board.

Project Manager (Sign/Date) JC