Introduction
Goal: Can we reconstruct the energy depositions of the proton in the
        brain if we are able to reconstruct the photons produced
        during this process ? [This document.]

---
Simulating particle interactions with Geant4
Geant4[*] simulation used to produce a simple model of a brain tumour:
4 components ('volumes'): air, skull, brain, tumour
made from simple geometric shapes
Protons generated at 180 MeV (configurable).
Particles are tracked until they leave a defined volume
   around the head →this is were a detector would be located
Output data stored in “root”[**] compatible format for analysis:
Hits (marks a Geant step): position, energy, 'volume'
Tracks: hits, particle id, generation process
[*] http://geant4.cern.ch/
[**] https://root.cern.ch/drupal/content/about

---
Geant Simulation
skin
skull
tumour
brain
particles only
particles
blue: charged
green: no charge
air
proton beam direction
bounding box (limit of the simulation)
z

---
Protons in the simulation
x and z position of each hit
(note scale)
E_kin at each point in the simulation
This information can be combined and converted to show the Bragg peak

---
Bragg peak

---
The (raw) data sample
100000 protons generated,
~20000 photons produced, ~15000 photons leave the head
(only these photons are being considered)

---
Photon properties
aligned with
beam direction
against beam
direction
symmetric in (X,Y) plane
(proton beam along Z)
perpendicular to beam
Phi
Theta

---
Photon properties
Photon scattering:
~ 50% of all photon point back to their origin
Photon kinetic energy
e.g. neutron capture in water

---
Photon properties
Distance last simulated proton his to first simulated photon hit in mm
This is dominated by
distance in z (along
the proton beam)

---
Proton →Photon
Proton: Last Hit
Photon: First Hit
tumour
skull

---
Vertexing
Last simulated hit (leaving air volume)
Photons
Next-to-last hit (usually leaving the head)
Extrapolate photons (usually
generated by different protons)
back towards tumour using
simulated hits outside the head.
Use midpoint of
the point of closest
approach as vertex.
Vertex
Note: In 3d space these
lines usually do not intersect

---
Vertexing
Algorithm:
Every ~200 photons calculate the vertex for each pair of photons
and enter into a 2d histogram.
True areas of increased photon generation should show up
with increased frequency.
These plots are for photons with E_kin > 1.0 MeV.
reconstructed vertices

---
z-axis constraint
As the deviation from the beam in the x,y plane is small, use point
of closest approach to z (=proton beam) axis of photons to reconstruct
proton interactions.
photon
z axis
On this and the previous plots,
the interactions at the entry point
to the skull (z= -200, y = 0)
are clearly visible.