## Slide 1: UK CMS Upgrade Oversight Committee
University of Bristol
Brunel University London
Imperial College London
Rutherford Appleton Laboratory
30 May 2018

## Slide 2: Overview
Snapshots of LHC & CMS status
  LHC delivered 50 fb-1 p-p in 2017
    2018 LHC start up has proceeded very well – already 10 fb-1 p-p @ 13 TeV by 17 May
      nice status report in CERN Bulletin 15 May
    The pixel problem of failing DC-DC converters was unresolved by examination, although the failure mode of the ASIC was identified – but not why.
    All units replaced in YETS
New CMS SP elected, from Sep 2018: Roberto Carlin (Italy)
  Deputies: P McBride (FNAL), L Malgeri (CERN)
Summary of progress in UK upgrade project
UK CMS Construction project proposal reviewed by PPRP
  Now awaiting decisions

## Slide 4
Some new results currently being obtained from additional devices inserted in CMS.

## Slide 6: News on upgrades
HGCAL TDR submitted and reviewed
  Approved by LHCC
Significant CMS activity on construction preparations and planning
  Many projects to manage, all at different stages, even if approved
  e.g. tracker organisation recently refined (next slide)
    One relevant consequence concerns approaching contracts and planning (our) future activities to match them, e.g. CBC
    However, no major issues at this stage for R&D
  Preparing reviews, as in the past, to monitor progress

## Slide 8
from D. Contardo CMS UG coordinator
MB 22 May

## Slide 9: UK R&D status

## Slide 10: Last 6 months
WP2: Tracker ASIC and readout
  In-house module and 2CBC3 2S-module tested in beams at end of 2017
  CBC3.1 design changes completed, and submitted for manufacture
      Delivery projected for 25 June
WP3: future hardware
  Considerable progress with new ATCA hardware, and infrastructure
WP4: HGCAL
  TDR submitted and approved, putting project on official footing
  UK work in optimising performance continuing to produce results
WP5: L1 track-finder
  Work on system development now progressing rapidly
  Stress test was proposed for FPGA track finder to confirm risks are low
    Some initial results from simulations

## Slide 11: WP2: CBC3 summary
All design changes incorporated into chip, vsn 3.1
  Submitted for manufacture early February
  Some administrative delays, so accepted 30 March with delivery 25 June.
    “delivery” means with bump metallisation completed
  This could be the final iteration and mask set for production
An order of 24 CBC3 wafers left foundry 16 May for bump metallisation
  Intended for module assembly prototyping
  Expected transport to CERN 26 June
    Wafers shared with CERN SCA chip (not usable), so 186 CBC3 per wafer
  Sufficient for many prototype modules to be constructed
    With CBC3s from engineering run, should be plenty for module prototyping despite Pactech metallisation problems
    Progress will be limited by other components, not CBC

## Slide 12: Recent CBC3 beam tests
Successful 2CBC3 2S-mini module test at FNAL in December
  120 GeV p beam
  Included operation at -20C
  Local pixel telescope allowed good track reconstruction
  Still much more to be tested in future
    e.g. high rate with pileup, and full geometrical coverage evaluation
Full size 8CBC3 module
  expected in autumn

## Slide 13
Results from December FNAL beam test of 2CBC3 module

## Slide 14: WP2 future
2S module development continues with CBC3
  Many components not final
    including hybrid where some fabrication problems were experienced
    Concentrator (CIC) chip remains main concern; first submission due end July
CBC3.1 verification (Q3 2018)
  Preparing station for CBC3 and CBC3.1 to identify KGD by automatic probing
  Planning final series of TID, low T, SEU tests to confirm changes
  Operation on full size module with sensor should provide final validation
Production manufacture
  Task for construction project, from April 2019
  But given delays with other parts, start date is uncertain
    Early ramp up useful to preclude (unexpected) manufacturing problems (cf. APV25)

## Slide 15: WP3: future hardware
Serenity ATCA prototype delivered
  Minor layout or manufacturing errors found but easily usable
    Layout issues fixed on recent respin, but some (annoying) assembly errors
  Testing is progressing rapidly, including software and firmware development
    Recently FPGAs on daughter cards mounted and exercised
Regular coordination meetings steering the activities

## Slide 16: WP3: future hardware
Two strands of development
  Demo Systems : Firmware & Software
    Q1 2018: Slow control and build tools for Xilinx UltraScale Devices
    Q2 2018: Basic infrastructure for algorithm development
  Serenity Prototype : Hardware
    Q2 2018: Provide Serenity hardware with low level firmware, plus basic infrastructure developed from “demo systems”
On schedule to meet milestones
Final Prototype: Generic
2018
2019
Demo Sys
Prototype
Pre-Production: Specialisation
2020

## Slide 19: WP3: future hardware
Deliver final prototype, including full infrastructure by Q2 2019
  Challenging in many aspects, particularly hardware delivery
Distribute to several groups
  Alternative processing nodes
    VU9P (TIFR) and KU15P (KIT) FPGAs
  Clock quality analysis (Saclay)
  Integration tests in CERN
  Continued firmware & software development
Final Prototype: Generic
2018
2019
Demo Sys
Prototype
Pre-Production: Specialisation
2020

## Slide 20: WP3: future hardware
Activities now broader than just UK
  Participants from India (TIFR), Germany (KIT), France (Saclay), Greece (Ioannina) and Italy (INFN)
Bi-weekly forum to coordinate the activities
  Started November 2017
  Working better than expected in most aspects
    e.g. collaboration on processing nodes, timing analysis, firmware

## Slide 21: WP4: HCGAL TDR
Main recent focus for HGCAL has been the TDR
    Submitted: Nov 2017
    Technical review by LHCC: Dec 2017 – Feb 2018
    Project review (cost, schedule, effort, risks) by UCG: Mar – Apr 2018
  Approval by CERN RB: Apr 2018, announced after OsC report submitted
As part of TDR, milestones and project organisation were reviewed and refined
  T. Virdee remains as overall Project Manager
  C. Seez and P. Dauncey remain as coordinators of the physics/reconstruction and trigger, respectively
The next major milestone is the EDR in mid 2020
  Must demonstrate use of Serenity for HGCAL BE

## Slide 22: WP4: HGCAL design studies
UK design studies have continued since the TDR
  Looking at detector/trigger optimisation to improve on TDR performance
Physics/reconstruction studies of depth segmentation underway
  Absorber thicknesses as a function of depth
  UK development of flexible standalone simulation for earlier studies has proved essential for rapid variation of thickness parameters
  Critical for finalising mechanical support structure; complete within 2018
Trigger clustering performance
  Do 2D clustering within each layer, then 3D clustering across layers
  Small change to 2D clustering algorithm resulted in significant improvement in pileup rejection
  Now working on 3D algorithm
Jet b/g rates: Old 2D
Jet b/g rates: New 2D

## Slide 23: WP5: L1 track finder
Bandwidth simulation studies between DTC and TFP
System Architecture
  Aim to pin down specifications of hardware, system design and interfaces by mid-2019 (CMS milestone)
Main consideration is margin & flexibility/scalability
  Cooling margin in blades, crates & racks
  Bandwidth margin:
    detector -> DTCs -> TFPs -> L1 correlator
  FPGA resource usage and margin
  Flexibility for additional processing or utilisation of newer FPGAs at later date
Working closely with WP3

## Slide 24: WP5: algorithms and firmware
Geometric Processor (GP) routes data according to η-φ tracking sector – now running in Ultrascale infrastructure (WP3)
Adapting track finding algorithms to reconstruct tracks with displaced vertices in x-y (aids electron track reconstruction, DM searches, etc)
Adapting and optimising TF algorithms to new system constraints and L1 requirements
Porting algorithms to Ultrascale/+ FPGA architectures
  including targeting higher operating frequencies

## Slide 25: L1 track-finder stress test
Proposed to simulate system beyond actual operational expectations
  To confirm that no dramatic failure mode might have been overlooked
    even though fairly extreme conditions already well studied in hardware and software
Early results already look very promising

## Slide 26: UK construction project
Proposal to PPRP submitted October, previously reported
  Reminder: Construction WPs, plus management activity
    WP2: Common technology
    WP3: Silicon tracker
    WP4: Calorimetry
    WP5: Trigger
Reviewed by visiting panel and all questions answered.
  Now awaiting outcome
  Would like soon to begin planning transition into construction project

## Slide 27: Conclusions
No actions from November meeting
Financial status
  Expenditure within targets with part of WA still available
    On track to conclude project within budget, and fully spent
  Part of WA for CBC design work and travel has been committed
    agreed with STFC how to handle this
  Largest financial uncertainty concerns any requirement for CBC3.1
    Should be clarified by end of 2018
Minor revised risk register, with explanations in report
We believe project is approaching a satisfactory conclusion in its final year

## Slide 28: Further information

## Slide 29: WP3: future hardware
Final Prototype: Generic
2017
2018
2019
Demo Sys
Prototype
MP-Ultra
Service Card
2016
Building Blocks
Full Prototype / Demo Sys
Pre-Production: Specialisation
2020
Spare Pictures