## Slide 1: UK CMS Upgrade Oversight Committee
Geoff Hall
University of Bristol
Brunel University
Imperial College London
Rutherford Appleton Laboratory
25 September 2012

## Slide 2: Overview
CMS status
LHC status and future plans
Revisit motivation for upgrades, in view of PPRP proposal
Review R&D background and current status
Recent WP progress
Finances
78 events pileup!

## Slide 3: CMS status

## Slide 4: Current Operational Status*
Chart: 
| muon CSC | muon DT | muon RPC | HCAL Barrel | HCAL Endcap | HCAL Forward | HCAL Outer | ECAL Barrel | ECAL Endcap | Preshower | Strips | Pixels
%Operational | 97.67 | 99.1 | 98.2 | 99.92 | 99.96 | 99.88 | 96.88 | 99.16 | 98.54 | 97.1 | 97.75 | 97.1
Pixel Tracker | Strip Tracker | Preshower | ECAL Barrel | ECAL Endcaps | HCAL Barrel | HCAL Endcaps | HCAL Forward | HCAL Outer | Muon DT | Muon CSC | Muon RPC
97.1% | 97.75% | 97.1% | 99.16% | 98.54% | 99.92% | 99.96% | 99.88% | 96.88% | 99.1% | 97.67% | 98.2%
*As of June 15 2012

## Slide 5: 4 July 2012
half design energy,
one third of integrated luminosity
five times higher pileup
than originally expected

## Slide 6: New physics
CMS has already made one major discovery
  still to prove it is a Higgs boson by measuring all its properties and couplings
  it was expected to require much more data
CMS has excluded large areas of phase space for the simplest SUSY models and new heavy vector bosons
  moving on to more complex models where mass of putative Higgs may give hints (“natural” SUSY)
  many other physics papers published…
Further investigations require much more data
  eg 2012 data insufficient to prove if 125 GeV boson spin 0 or 2
  searching for rare phenomena: ~2B events will be stored in 2012

## Slide 7: lhc status

## Slide 8: Comparison 2010 – 2011 - 2012
2010: 0.04 fb-1
  Machine commissioning
2011: 6.1 fb-1
  Production
2012: 13 fb-1 so far
  Higher energy
  Smaller beta*
  Increased bunch current
8

## Slide 9: LHC future plans
LHC operational conditions in 2012
  8 TeV, 50ns bunch spacing, Linst~8 x 1033 cm-2s-1
    target ~25 fb-1 with LS1 delayed 6 months
Long term plan: Long Shutdowns (later dates may change)
  LS1: March 2013-2015 - upgrade to full energy
    14 TeV, 25 (50?) ns bunch spacing, Linst< 2.5 x 1034 cm-2s-1
  LS2: 2018 - improve collimation and other machine elements
    14 TeV, Linst< 4(?) x 1034 cm-2s-1
  LS3: 2022 - upgrade for very high luminosity
    14 TeV, Linst~5 x 1034 cm-2s-1 (levelled)
LHC machine consistently outperforming expectations
  no scope for relaxation if physics reach to be maximised

## Slide 10: Motivation for Upgrade

## Slide 11: The need for upgrades
CMS and the LHC are working so well, with outstanding results, so why is an upgrade needed?
  maintain physics performance in high pile-up conditions
    trigger must maintain low pT/E thresholds and 100 kHz rate
    inner detector will be damaged by radiation
    pixel tracker loses data at high rate
Why is it needed now? (+ time needed to build the systems)
  luminosity much higher than expected, and much sooner
  pile-up has dramatic impact on trigger
  tracking degrades significantly
  original designs were limited by technology of the time
Eventually (~2022) a brand new tracker is required
  must be ready for large scale production by 2017

## Slide 12: Luminosity
Nearly all the parameters are variable (and not independent)
  Number of bunches per beam kb
  Number of particles per bunch 
  Normalised emittance n
  Relativistic factor (E/m0) 
  Beta function at the IP  *
  Crossing angle factor F
    Full crossing angle c
    Bunch length z
    Transverse beam size at the IP *
Interaction Region
Energy
Total Intensity
Beam Brightness
c
Presently F  0.8

## Slide 13: Comparison with nominal & pile-up
pile-up ≈ number of events per bunch crossing
  ie µ = Ns
  Tracker also sees particles looping in B field
For same L, 2x bunch spacing -> 2x pile-up
CMS designed for 14 TeV, L = 1034 cm-2s-1 and 25 ns
Parameter | 2010 | 2011 | 2012 | Nominal
N ( 1011 p/bunch) | 1.2 | 1.5 | 1.6 | 1.15
k (no. bunches) | 368 | 1380 | 1380 | 2808
Bunch spacing (ns) | 150 | 75 / 50 | 50 | 25
en (µm rad) | 2.4-4 | 1.9-2.4 | 2.2-2.5 | 3.75
* (m) | 3.5 | 1.5  1 | 0.6 | 0.55
L (cm-2s-1) | 21032 | 4.01033 | 7.61033 | 1034
 | 3 | 19 | 35 | 23
13

## Slide 14: Examples of physics impact
Tracker degradation gives overall loss of data/quality
  and, e.g., significant losses of b quark jets
Potential losses at trigger level
  WH associated production
  trigger on W (single e/µ) to measure H properties without bias
    pT thresholds will rise significantly before LS2 (next slide)
  For Higgs couplings measurements
  may only be possible using VBF production topology
  trigger on correlations between jets, especially forward jets
  pile-up is extreme.

## Slide 15: Sample trigger menu from current L1 trigger
Algorithm | 8 TeV 7E33 ~25 PU |  | 14 TeV 2E34 50 PU | 
 | Thresh (GeV) | Rate (kHz) | Thresh (GeV) | Rate (kHz)
Single EG | 22 | 10 | 46 | 10
Single IsoEG | 18 | 9 | 31 | 9
DoubleEG | 13, 7 | 9 | 22, 12 | 9
Single Muon | 16 | 9 | 50 | 9
Dble Muon | 10, open | 5 | 35, open | 5
EG+Mu | 12, 3.5 | 3 | 21, 6 | 3
Mu+EG | 12, 7 | 2 | 25, 15 | 2
SingleJet | 128 | 2 | 188 | 2
DoubleJet | 56 | 10 | 132 | 10
QuadJet | 36 | 2 | 96 | 10
Double Tau | 44 | 2 | 56 | 2
MET | 36 | 7 | 84 | 7
HTT | 150 | 2 | 511 | 2
Multi-jet trigger thresholds affected by both √s and PU
Single lepton thresholds are very high
Example 14 TeV trigger menu
Using current bandwidth allocation
Based on MC - still needs to be fully validated & finalised
Combined rate of current single lepton triggers only
~ 140 kHz at 14 TeV 2E34
Cannot maintain current thresholds with current L1 trigger at 14 TeV 2E34

## Slide 16: IMPACT on cms

## Slide 17: Tracking at high pileup
Tracking efficiency is reduced – affects everything
Fake track rates are increased
Primary vertices merge
Resolution worsens, due to wrong hits
Increased CPU and memory use
Inner pixel layers: dynamic data loss affects track seeding

## Slide 18: L1 Total Cross Section vs. Luminosity (Limits of Prescale Columns)
“6E33” column to
6.7E33
“7E33” column to 7.7E33
100 kHz(*)
90 kHz
(*) Deadtime limits to 90 kHz
“8E33” column to ~8.4E33

## Slide 19: Improved Pile-up Handling in L1 Jets
Increased jet seed threshold to 5 GeV in Global Calorimeter Trigger since June Technical Stop
Significantly reduces exponential rise in xsec
GCT team

## Slide 20: But… Problem is only Postponed…
Blow-up seen to return at higher pile-up (special fills)
  Can further increase the seed threshold and jet threshold in HT
  But better yet is an upgraded L1 trigger !
Lumi @ 50ns: 1E34 1.4E34
0.5 MHz @ 50 ns !
C.Battilana

## Slide 21: UK R&D since 2009

## Slide 22: UK CMS upgrade R&D achievements
WP1 – software and simulations
  IPbus (µTCA control) (10/11) adopted as common CMS-wide standard (02/12)
  simulation studies for trigger and tracker upgrades in TDRs (09/12)
WP2 – Outer microstrip tracker readout
  CBC 128 channel ASIC (03/11) developed in single design iteration & evaluated
  CBC2 256 channel ASIC submitted (07/12), with trigger data, due (10/12)
  DAQ & FED studies, with CBC module beam tests (09/11)
WP3 – L1 calorimeter trigger system
  Mini-T5 (02/10) & MP7 (07/12) processor boards delivered and working
  CMS review recommended UK hardware for future baseline (12/11)
  original new trigger architecture proposed (02/11) and demonstrated (03/12)
WP4 – pixel DAQ
  Long experience in Tracker DAQ and DQM
  UK proposal to design and deliver new pixel FED accepted (11/11)
    modified trigger hardware, IPbus and pixel ROC test beam experience (7/12)

## Slide 23: Online Control System
IPbus: scalable, hierarchical software/firmware system

## Slide 24: Track reconstruction code optimisation
Example of ongoing efforts to improve high pile-up performance
  also relevant to current operation
New search method to reduce time spent in the two [pixel] triplet seed generators based on k-D trees
  Using k-D tree code in both generators gives significant decrease in CPU time
  negligible reduction in tracking efficiency
 | Standard | Large Tip k-D tree | LargeTip and HLT k-D tree
LargeTIPGenerator | 3.94% (28s) | 0.83% (6s) | 0.84% (6s)
HLTGenerator | 1.37% (10s) | 1.38% (10s) | 0.74% (5s)
CombinedHitGenerator | 5.31% (38s) | 2.20% (16s) | 1.58% (11s)

## Slide 25: WP2: Phase II Outer Tracker readout
APV plane
CBC sensor
5 mV / division
beam profile
CMS Binary Chip: 130nm CMOS
  128 channel binary ASIC, non-zero suppressed
  Amplifier, pipeline, memory, logic, control
  many new features, excellent performance
  tested in beam with 5cm µstrips
5 cm
p-on-n
150 mm pitch
320 µm thick

## Slide 26: CBC2 design
250 µm pitch C4 layout
  back edge wire-bond pads for wafer probe
254 channels
  allows correlation between 127 top & 127 bottom strips
architecture based on CBC prototype
  front end, pipeline, readout architecture, powering features, …..
submitted July 2012
  wafers expected ~ October
tested, functional CBC2 is final deliverable of current Upgrade programme
11 mm
5 mm

## Slide 27: 2S PT-module with CBC2
Track & trigger module under development with CERN, Lyon, ..
  CBC2 logic correlates hits on two sensors to reject those from low pT tracks
    many issues to construct such a module
27
8 x 254 channel chips
bump-bonded to hybrid
8 x 254 channel chips
bump-bonded to hybrid
chips on top surface only
signals from lower sensor
via’d through substrate
~5 cm
90 µm pitch strips
sensors wire-bonded
above and below
~5 cm
concentrator
&
controller
two layers of sensors

## Slide 28: WP3: calorimeter trigger
Brand new architecture proposed (but hardware is agnostic)
  possible because of technology progress (FPGAs & links)
  TMT = boundary-less calorimeter processing
  decision postponed but concern about trigger after LS1 growing
    actions to install complete new optics advancing
Demonstrator using mini-T5 (Virtex-5 FPGA)
  emulates ¼ of present CMS calorimeter trigger
  TMT versions of present algorithms (much faster)
  HL-LHC algorithms already in firmware
  latency (potential concern) measured
MP7: final board delivered August 2012 (Virtex 7 FPGA)
  already producing impressive results in very early tests

## Slide 29: Trigger Architecture
Options: Conventional Trigger vs Time Multiplexed Trigger
  TMT: all calorimeter data to single processor
  Allows more flexibility in trigger design & avoids boundaries and data sharing
CT
TMT

## Slide 30: MP7 Prototype Preliminary Results
1Tb/s - All 96 optical links operating at 10Gb/s simultaneously
  x4 bandwidth of any previous card in CMS
  1.0 - 1.4 Tb/s of optical I/O (Tracker FED ~ 25 Gbps)
  (TWEPP 2012 suggests this board is well in advance of anything else…)
All peripherals operating (RAM, CPLD, MMC, etc)
Cooling will be improved
  verify contributions to power consumption when diagnostics available

## Slide 31: MP7 - Preliminary results
Clean optical eye (left) and electrical received eye (right).
  pre-emphasis in the optical receiver, should improve the eye even more.
PCB manufacturing improvements are possible should we need them.

## Slide 32: Demonstrator
PP0
MINI-T5
(Main Processor)
x 2 Main-Processors
Patch Panel
ECAL & HCAL Trigger Primitive Data would enter here
AMC13
PP1
PP2
PP3
PP4
PP5
PP0
PP0
x 24 Pre-Processors
MINI-T5 (6x PreProcessors)
MINI-T5
(Main Processor)
MCH
Standard Services
Custom Services
MINI-T5
(Global Trigger)
  1/4 CMS at 24 bit/tower resolution for every 6th BX

## Slide 33: Latency – Time-Multiplexed CMS GCT
PP algo
PP GTX
MP GTX
MP Align
MP Algo
MP GTX
GT GTX
GT Align
MP output valid flag
GT input valid flag
PP output valid flag
Total latency is:
1 Link latency (PP to MP) | 6.5 BX | 161.6ns
1 Algorithm latency | 3.7 BX | 92.8ns
1 Link latency (MP to GT )† | 7.5 BX | 182.4ns
1 Time-Mux period | 10 BX | 250 ns
Total | 27.7 BX | 686.8 ns
Look at that – the maths works, phew! 
†Making allowances here for the firmware bug

## Slide 34: WP4: pixel DAQ
Pixel detector will be replaced at end of 2016
  improved performance for high pile-up environment
TDR released with UK proposal for pixel FED & DAQ responsibility
  subject to PPRP approval
  builds on UK expertise in Tracker DAQ and R&D to date from all existing WPs, with sharing by all UK groups
  WP1: IPbus & simulations
  WP2: SFED development
  WP3: mini-T5/MP7 hardware & firmware
Very positive response from CMS
  UK is highly regarded, and we gain expertise in strategic area
  strengthens pixel project & matches long term µTCA adoption (we are “experts”)

## Slide 35: Phase I pixel upgrade
  less material & better layout means less conversions & interactions
  better IP resolution and b-tagging efficiency
  improved seeding efficiency & lower fake rates from extra tracking layer
  4th layer provides better track projection to the strip tracker
  higher readout efficiency and less deadtime with new ROC and digital readout chain
Replacement is a lower mass detector with 4 barrel layers and 3 endcap disks per side

## Slide 36: Phase I pixel upgrade
  substantially reduced detector mass, despite twice number of channels
    CO2 cooling, improved mechanics, optimised layout of services
  b-jet efficiency improvement of 30%, for a 1% fake rate at 100 PU
Radiation length vs. Eta
Dots – Upgrade
Green – Current
100 PU

## Slide 37: New ROC and readout chain
New ROC and readout scheme required for efficient operation up to 100 PU
  estimated ~50% data loss at 100 PU (50 ns bunch spacing, 2x1034 cm-2s-1 at r = 3.9cm)
  requirement is for < 3% data loss at new 2.9cm reduced radius
ROC
TBM
token in
token out
160 Mbps data
OH
400 Mbps 4b/5b encoded data
optical link to FED
- increased buffer sizes and improved hit buffering architecture in ROC
- 8 bit ADC to digitise pulse height information within ROC
160 Mbps digital readout at ROC
data on a module multiplexed and encoded onto twisted fibre with new TBM
new optical hybrids for high speed digital transmission at 400 Mbps
module
service cylinder

## Slide 38: Phase I pixel FED
New DAQ required
  new digital optical links
  more channels so higher data throughput
FED prototype based on MP7
  mezzanine cards for prototyping and maximum flexibility
  reusing MP7 design mitigates risk and benefits from firmware & software investment
FMC1
FMC2

## Slide 39: Pixel beam telescope
Modular system
  Variable number of ROCs
  Variable readout system
  Standard ROC carriers
  Easy to replace ROCs
Successfully used in beam test in July 2012

## Slide 40: Pixel DAQ board
First FED firmware test bed
  Xilinx evaluation board with custom adapter
First application
  high rate test beam in October

## Slide 41: PPRP proposal: Work Programme
Builds and continues R&D progress to date
  detailed plans based on (best knowledge of) CMS schedule
WP2: prepare for construction of Phase II tracker
WP3: construct new calorimeter trigger
WP4: deliver pixel FEDs and implement new DAQ

## Slide 42: WP2 objectives: next ~ 6 years
complete CBC development for SS-pT module
  bring chip to final state ready for mass production
develop hardware & software for mass production test
  extensive experience from LHC production
major role in definition, construction and evaluation of prototype modules
  in collaboration with groups responsible for other module components
contribute to ancillary chips development and PS-pT (strixel layer) module
contribute to tracker construction
  procurements, integration and commissioning
Geoff Hall
CMS UK OSC Mar 2012
42

## Slide 43: WP3 deliverables
Geoff Hall
CMS UK OSC Mar 2012
43
No | Month | Deliverable
M3.1 | 9 | Updated algorithms and software for current L1 calo trigger
M3.2 | 15 | CMS L1 Calo trigger ready for post-LS1 running
M3.3 | 24 | Design studies for > 2x 1034 cm-2s-1 trigger ready; architectural choices made by CMS; sign-off point on > 2x 1034 cm-2s-1hardware production
M3.4 | 40 | Hardware systems ready for > 2x 1034 cm-2s-1 trigger
M3.5 | 48 | > 2x 1034 cm-2s-1 trigger in operation
M3.6 | 60 | Technical design of post-LS3 trigger complete; sign-off point on LS3 prototype production
M3.7 | 72 | Delivery of track trigger prototype

## Slide 44: WP4 deliverables
Geoff Hall
CMS UK OSC Mar 2012
44
No | Month | Deliverable
M4.1 | 6 | prototype FMC-FED hardware available
M4.2 | 18 | standalone prototype FED, multi ROC readout
M4.3 | 18 | standalone prototype FEC, multi-module control
M4.4 | 24 | demonstrator FED & FEC with readout & control of pilot blades
M4.5 | 24 | demonstrator fast link integrated with central DAQ hardware
M4.6 | 33 | final FED hardware ready for production
M4.7 | 39 | final firmware & software for full system ready for deployment
M4.8 | 45 | delivery of full Pixel DAQ

## Slide 45: Summary
Very good progress continues in all WPs
  6 year plan now incorporated in PPRP bid, which is under review
CMS and LHC upgrade planning
  pixel TDR released, Trigger TDR ~March 2013
Finances
  spending increased: commitments on MP7 & CBC2
    Working Margin now £120k and will reduce in remaining 6 months
    Need more MP7s for new demonstrator
    Reserve in case of CBC2 problems
  SSC reporting changed again: no PPD staff costs visible
  Travel now handled by universities
Not yet finished the R&D but the UK investment has been timely, immensely helpful and put us in a strong position for the future.
  Thanks!

## Slide 46: Further information

## Slide 48: Long Shutdown 1
End March 2013 – November 2014
Consolidation for 6.5 – 7.0 TeV operation
  Measure all splices and repair defective ones
  Repair of magnet interconnects after 2008 event with new design (clamp, shunt)
  Finish installation of pressure release valves
  Exchange of weak cryo-magnets and DFBAs
  Relocation of equipment to reduce radiation effects on electronics
  Installation of collimators with integration beam position measurement, injection absorbers refurbishment
  Injection kickers reduction of heating
  Experiments consolidation and upgrades
Plus a lot of other work ongoing
  Cryogenics, Quench Protection, electrical infrastructure, cooling & ventilation, Radio Frequency, beam dump absorber & magnet, change of dump switches (radiation), electron cloud mitigations …
48

## Slide 49: Potential Performance after LS1
Determined by the performance of the injector chain
Different collimator scenarios, not detailed here
LHC Injector Upgrade (LIU) fruits after LS2
 | Number of bunches | * [m] | Half X-angle [rad] | Ib SPS | Emit SPS [um] | Peak Lumi [cm-2s-1] | ~Pile-up | Int. Lumi [fb-1]
25 ns | 2800 | 0.50 | 190 | 1.2e11 | 2.8 | 1.1e34 | 23 | ~30
50 ns | 1380 | 0.40 | 140 | 1.7e11 | 2.1 | 1.8e34 * level | 81 * level | ?
25 ns low emit | 2600 | 0.40 | 150 | 1.15e11 | 1.4 | 2.0e34 | 48 | 52
50 ns low emit | 1200 | 0.40 | 120 | 1.71e11 | 1.5 | 2.2e34 | 113 | ?
Presently at 4 TeV, * = 0.6 m, half X-angle 145 rad

## Slide 50
Latency – Time-Multiplexed CMS GCT
BX 0 |  |  |  |  |  |  |  |  |  | BX 10 |  |  |  |  |  |  |  |  |  | BX 20 |  |  |  |  |  |  |  |  |  | BX 30 |  |  |  | 
Source card |  | Source to Leaf card link |  |  |  | Leaf card deserialization |  |  |  | Jet Finder Algorithm |  |  |  |  |  |  |  |  |  |  | Wheel card |  |  | Concentrator card |  |  |  | Concentrator to GT link |  |  | GT deserialization |  |  | 
Original GCT timing specification
BX 0 |  |  |  |  |  |  |  |  |  | BX 10 |  |  |  |  |  |  |  |  |  | BX 20 |  |  |  |  |  |  |  |  |  | BX 30 |  |  |  | 
 |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (1-3) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (4-6) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (7-9) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  | Sort in other direction (if necessary) |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Time Muliplexing |  |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (10-12) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (13-15) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | PP to MP link, deserialization and alignment |  |  |  |  |  | Jet Finding (16-18) |  |  |  | Sort 1D |  | MP to GT link, deserialization and alignment |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMT GCT timing using Mini-Ts
Using the 6 data frames needed instead of the 10 used in the demonstrator system
Fixing the GT deserialization bug
Adding the 1D sort
TMT latency, 23 BX
Data flow through one Main Processor

## Slide 51: Sample trigger rates from current L1 trigger
Single e/γ trigger
      Black - 14 TeV MC (50 PU)
        Red - 8 TeV data (66 PU)
Poor control of lepton rates at high thresholds due to poor pT resolution
HT (ET sum of jets)
Black - 8 TeV data (66 PU)
        Red - 8 TeV data (45 PU)
Rates shown for Linst=2×1034cm-2s-1
Single muon trigger
Black - 14 TeV MC (50 PU)
        Red - 8 TeV data (66 PU)
Jet trigger rates strongly dependent on PU

## Slide 52: CBC Architecture
Notes: Could use fastOR and an external Read for readout of coincidence data:
Always @(fastOR posedge)
if (Read==0) write data;
else;
Always @(read posedge) readout data;
Always @(read negedge) reset data;

## Slide 53: simplified WP2 Gannt
Geoff Hall
CMS UK OSC Mar 2012
53
CBC2 test
CBC3 design & production
CBC3 test
2013
2014
2015
2016
2017
CBC4 design & production
CBC2
available
here
CBC4 test
CBC4 full wafer masks and engineering run
CBC2-based module studies
CBC3-based module studies
CBC3 should be very close to final chip - available late 2014
  includes architecture for formation and high speed transmission of stub information
CBC4 pre-production iteration (2015/16) allows final bug fixes before full-wafer engineering run in 2017