## Slide 1: UK CMS Upgrade Oversight Committee
Geoff Hall
University of Bristol
Brunel University
Imperial College London
Rutherford Appleton Laboratory
12 November 2013

## Slide 2: Overview
Snapshots of CMS & LHC status
  Recent summaries at October RRB & ECFA HL-LHC workshop
  LHC: LS1 on schedule and machine very confident to be ready for restart
  Plans beyond that are still uncertain
    funding & scheduling issues
    overview of experiment requests compiled by S Bertolucci for RRB
Summary of UK upgrade project
  Recent WP progress
Finances and other issues

## Slide 3: Spin-Parity
0- Excluded @ 99.8% CL
0+ vs. 0-
ALL ARE CONSISTENT
WITH JP = 0+
0+ vs. 2+
2q =
New Spin 2 Exclusions
CMS
CMS
3
New Spin 1 Exclusions
0+ vs. 1+
Notable recent results

## Slide 5
F Bordry

## Slide 9: CMS Status in a Nutshell
  Phase 1 Upgrades
    Common item costs were reviewed and revised downward
    Much progress and on schedule
  Long Shutdown 1 (LS1), including many phase 1 upgrade tasks
    Work goes well
  Run 1 Physics
    Analyses well on track to meet our goals
  Run 2 Preparations
    Progress on cpu-efficiency, tools and procedures
  Phase 2 Upgrades
    Preliminary scope and cost has been documented, presented today
9

## Slide 10: Technical Coordination: LS1 project
Cost to complete LS1 common project is within original estimates.
Activities at P5: On-going with good progress
  Tracker colder
  ME 1/1 revision
  HCAL revision part I
  YE4 installation
Other activities progressing well too
  CSC assembly, testing, installation
  RPC assembly and testing
  Pixel cooling system pre-assemblies
  Beampipe
All OK, except for delay recovering beampipe incident, again!
  On two occasions, during removal from the EB welding-facility, pipe broke at a weld.
    Discussing with vendor to make sure to get it right this time.
  Specialized tooling for conical section probably necessary
  Still can make schedule if it does not happen a third time.
  All costs being borne by vendor
Cone
Cylinder
10

## Slide 11: CMS Upgrade program in one slide
LS1
2013-14
LS2
2018
LS3
2022-23
LS1 consolidation: Complete/consolidate for nominal LHC beam conditions: Prepare for: 13 TeV, 1034 Hz/cm2 , Ave. Pileup (<PU>)∼25
Complete Muon system (4th endcap station) and improve readout electronics
Replace HCAL photo-detectors and backend electronics in a couple of regions
Make it possible to operate the Tracker at -20∘C
Phase 1 upgrades: Prepare for 1.6 x 1034 Hz/cm2 , <PU> ∼40,  200 fb-1 by LS2 Prepare for 2.5 x 1034 Hz/cm2, <PU> ∼ 60,  500 fb-1 by LS3
New L1-trigger system ready for 2016 data taking
New Pixels ready for installation in 2016/17 Year End Technical Stop (YETS)
Install new HCAL photodetectors and electronics in 2015 YETS and LS2
Phase 2 upgrades: Prepare for ≳ 5 x 1034 Hz/cm2, PU 140 to 200
    Total of 3000 fb-1 in ∼10 yrs operation
  Replace subsystems that no longer function due to radiation damage
    Tracker including Pixels, Endcap calorimeters
  Maintain physics performance at very high PU
    New Electronics and Trigger, enhanced detector coverage
11

## Slide 12
CMS Phase 2
The minimal set of upgrades that replace degraded systems and provide requisite physics sensitivity for the highest priority physics goals in the face of 140 pileup events per bunch crossing, and to assure the ability to run up to at least 3000 fb-1
12

## Slide 13: CMS@HL-LHC
Projections for Higgs couplings
  2-10% with HL-LHC
Rare Higgs decays studied*
  H  µµ at > 5σ with HL-LHC
Low Mass Stops
  Already with 300 fb-1, discovery potential direct production mode up to ~900 GeV
2-10% precision on Higgs couplings
13
*to appear in final draft of WP

## Slide 14: Phase 2 Upgrades
Replace Endcap Calorimeters
Muon system
Tracker
Trigger/DAQ
GEM Glass RPCs
Extended h coverage
New DT minicrates
Higher granularity
Less material
Better pT resolution
Extended h coverage
Track trigger at L1
New FE and RO
L1 up to 1 MHz
HLT up to 10 KHz
Tracking at L1

## Slide 15: CMS Phase 2: Conclusions Thus Far
Systems that do not need to be replaced
  Barrel calorimeters, HF and muon chambers will perform to 3000 fb-1
Systems that must be replaced are
  Tracking system and Endcap calorimeters must be upgraded in LS3
    Neither survives much beyond LS3
  Endcap calorimeters:
    Extensively studied ways to recover EE crystals.
      No practical solution found.
    With phase 1 upgrades the HE survives until LS3 but not much beyond.
  Electronics for specific subsystems
15
Relatively new requirement

## Slide 16: Phase 2 Tracker: conceptual design
Higher granularity, less material
  Track reconstruction at PU 140 and beyond
  2 sensor “Pt-modules” to provide L1 trigger information at 40 MHz for Pt≥2GeV
Pixels: sensors 100 µm thick
  Smaller pixels: ~30 x 100 µm
  4 barrel layers, 10 disks to cover up to ∣η∣= 4
R&D activities: All components
  Sensors and readout electronics
  Prototype of 2S modules ongoing
  BE track-trigger tbd
x
y
z
“stub”
Trigger track selection in FE
16
  Trigger - major new endeavour

## Slide 17: Endcap Calorimeters
Two approaches
  Maintain tower geometry - develop rad-tolerant solutions for 3000 fb-1
    EE towers e.g. in Shashlik design (crystal scintillator: LYSO, CeF)
    Te build HE with more fibers, and rad-tolerant scintillator
  Alternative geometry/concepts
    Potentially improved performance and/or lower cost
      Dual fiber read-out: scintillation & Cerenkov (DROC) – alla DREAM/RD52
      Particle Flow Calorimeter (PFCAL) – following work of CALICE
17
Early stage. R&D urgent
Notes:     Dual fiber read-out: scintillation & Cerenkov (DROC) – following work of DREAM/RD52
      using doped/crystal fibers - allows e/h correction for improved resolution
    Particle Flow Calorimeter (PFCAL) – following work of CALICE
      using GEM/Micromegas – fine transverse & longitudinal segmentation to measure shower topology

## Slide 18: Phase 2 Cost Exercise
Used reasonable assumptions
  Materials, channel counts, etc.
    No contingency included
Breakdown of costs
  Replacement of radiation damaged detectors ~ 75%
  Retaining performance in very high pileup environment ~ 15%
  Extending coverage < 10%
Staging under study
  Options are limited
18

## Slide 19: Phase 2 Spending Profile
Profile driven to a large extent by the LS3 start and duration
  Tracker and Endcap calorimeters need to be competed in LS3
An extra year flattens the profile. Diminishing impact beyond that.
Phase 1: 66% of spending will be complete by end of 2014
Blue = the current LHC baseline schedule. Orange and Purple represent alternative LS3 dates.
19
Chart: MCHF
| 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0
LS3:calendar 2022-2023 | 0 | 12.84 | 37.7058 | 59.0164 | 62.0424 | 57.8258 | 27.604 | 11.997 | 0
LS3:calendar 2023-2024 | 0 | 8.242 | 31.5983 | 46.7604 | 50.5943 | 51.953 | 45.0815 | 22.805 | 11.997
LS3:mid2023 - end2025 | 0 | 8.242 | 31.5983 | 43.9298 | 46.3855 | 46.9413 | 44.3882 | 28.1458 | 15.4015 | 3.999
Phase 1 | 6.188 | 2.049 | 4.625
Representative spending profiles for different schedules for LS3

## Slide 20: UK R&D status

## Slide 21: Evolution of objectives
Original goal
  new – improved - tracker with similar angular coverage, constrained by re-using existing services
  provide some part of tracker data to L1 trigger to contain rate to 100 kHz
More recent developments
  Baseline Tracker design now adopted
    “conventional” barrel-endcap layout looks optimal
  but CMS exploring enhancing forward region physics as well as standard physics programme
  uncertainty if L1-track triggering will reduce rate to 100 kHz in 6.4µs
    ideas (and detector requirements) not yet validated by simulations
    possible objective of L1 readout up to 1 MHz/10-20µs
    both approaches require on-detector data reduction

## Slide 22: WP2 objectives and status
Complete CBC & 2S-module development for construction project
  development, with collaborators, of 2S module, and evaluation studies
    to be ready for mass production with hardware and software for large scale acceptance tests
  contribute to PS-module readout development
  FC7 for CBC module readout
    generic-type board, to be utilised by multiple projects, in collaboration with CERN
Good progress with CBC2 evaluation
  chip is functioning well and suitable for prototypes
  2 wafers so far tested. Plenty of chips in hand
  First (ever!) beam test of PT-module imminent
    DESY 25-30 November

## Slide 23: CBC -> CBC2: New features
  250µm pitch C4 layout
    aim for commercially assembled module
    some gains in bond inductance
    back edge wire-bond pads for wafer probe
  254 channels for 127 + 127 strips
  correlation logic for stub formation
    between top & bottom strips
    vetoes wide clusters
  Test pulse
    no time to implement on CBC
    & other minor circuit improvements
  Improved DC-DC (CERN)
  received Jan 2013 – fully functional
DC-DC
LDO
pipeline
+
buffering
254 amplifier/comparator channels
CWD, offset correction and colleraltion logic
bandgap
bias gen.
254
inputs
5 mm
11
mm
inter-
chip
signals
inter-
chip
signals
Reminder only

## Slide 24: 2S PT-module with CBC2
Track & trigger µstrip module for outer tracker region
  CBC2 logic correlates hits on two sensors to reject those from low pT tracks
24
8 x 254 channel chips
bump-bonded to hybrid
8 x 254 channel chips
bump-bonded to hybrid
chips on top surface only;
signals from lower sensor
via’d through substrate
~5 cm
90 µm pitch strips
sensors wire-bonded
above and below
~5 cm
concentrator
&
controller
two layers of sensors
low mass, high density interconnect layer
Reminder only

## Slide 25
Stub finding Logic
Stubs shift register
latch
@40MHz
Individual mask for noisy channels
→254b from I2C reg.
(can be also used to inhibit coincidence logic)
Need to be able to inhibit stub shift register operation
→1b EN from I2C reg.
254-OR of channel outputs to signal any activity on chip
127-OR of stubs to control the stubs SR readout

## Slide 26: Result with test pulse
  Proves basic functionality
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
1
1
2
2
3
3
4
4
5
5
6
6
7
7
8
8
9
9
10
10
11
11
12
channel
on chip
channel
on layer 1
channel
on layer 2
8 test
groups
shown in March OSC

## Slide 27: 2S mini-module
Several prototypes assembled with two sensors
  Under test in lab since July
  Preparing for DESY beam test in two weeks time

## Slide 28: 2S mini-module in lab
Some illustrations of logic tests using b source follow

## Slide 29
CBC2 triggered data output
CBC2 trigger output
scintillator/PM signal
hits in the data stream

## Slide 30
CBC2 triggered data output
2 consecutive hits
=> track passed through
strips directly above
each other
50 ns

## Slide 31
single strip clusters
offset by 1 strip
75 nsec

## Slide 32
2 strip cluster in one plane
correlates with 1 strip cluster
in the other

## Slide 33
hybrid temperature
sensor
Peltier
LV power
Control &
Readout
(LVDS)
Level Shift
test-beam module

## Slide 34
FC7
for qualifying CBC ASICs & prototype modules in beam
also used for making precise measurements on performance of next generation LHC collimators
new generic µTCA DAQ board
flexible – support two FMC-compatible mezzanine cards accessible from the front panel, compatible with µTCA and µTCA for CMS
will replace TTC system in 2014,
pixel FEDs & FECs in 2017;
future DAQ for Phase II proto-CBC modules
status: first prototypes passed initial testing, all serial links running well at 10Gbps, all I/O validated
0.2 Tb/s bandwidth over 20 front panel serial links
128 front panel user I/O, up to 1.2 Gb/s per pair
CMS upgrades – beam telescope
M. Pesaresi (Imperial)
P. Vichoudis (CERN PH-ESE)

## Slide 35: Rough road map
CBC1
- analogue front end in 130nm
wirebonded
binary logic
- L1 triggered readout only, non-sparsified
CBC2
C4 bump-bonded
full hit correlation logic
L1 triggered non-sparsified readout, fast trigger OR
CBC3
full readout architecture defined
final data format
additional correlation logic
CBC4
optimisation
final version
2011
2012
2014
2016
2S-Pt prototype module studies
2S-Pt final module studies
start production
2017
2015
2013
as foreseen in proposal

## Slide 36: WP2 planning
CMS goals based on TP [2014] and Tracker TDR [2016], then construction
Excellent CBC progress begs some questions:
  can we rely on this schedule, given planning & funding situation?
  will be CBC be ready too soon? could the requirements change?
  will engineering effort be used too soon?
  can the tracker construction (or TDR) start without proven PS module?
no urgency at present for CBC3
  would finalise data format and improve a few details
  plenty of CBC chips available for modules
  much to be done in evaluation both module and chip
    2S and logic performance
    SEU and irradiation
review milestones and objectives in coming months before next OSC

## Slide 37: WP3 objectives and status
Improvement of calorimeter trigger for next running period
  based on
Time Multiplexed Trigger (now adopted)
  commissioning in parallel with operation of existing trigger
Design of track-trigger for HL-LHC
  and technology demonstrator
Recent progress
  Very successful TMT slice test at end September
    UK hardware used for both Layer 1 & Layer 2
    A lot learned about firmware & tools
    Algorithms implemented and latency measured
  Significant simulation work on future algorithms
  Several iterations of MP7
    some fabrication issues which need care, but not show-stoppers

## Slide 38: Overview: calorimeter trigger
Commissioning of calorimeter trigger in parallel in 2015
  Necessary to install oSLB/oRM during LS1 (complex operation)
  Necessary to install passive optical splitters for HCAL (LS1 and YETS
A Tapper
LHCC referees meeting May 2013

## Slide 39: Time-multiplexed trigger
Conventional Trigger
Time-Multiplexed Trigger
DEMUX
GT
L1 decision
The Time-multiplexed architecture allows all data to arrive in geometric order:
  Towers at given φ are always the same bits on the same optical links
  Towers arrive in order of increasing |η|
This converts a 2D geometric problem to a 1D problem
Also only need to develop 1 FPGA design
Chosen by CMS as architecture of Phase 1 Trigger upgrade
Project milestone from TDR to demonstrate working concept in September 2013
TMT test took place starting 30th September in building 904
Bristol, Imperial, RAL, LLR involved
Complete set of results @
https://indico.cern.ch/getFile.py/access?contribId=6&sessionId=1&resId=0&materialId=slides&confId=277887

## Slide 40: TMT layout
PP-B
PP-T
MP
Demux
Simulating multiple PP cards with a single MP7
Simulating multiple PP cards with a single MP7
MP7’s used here as PP’s, CTP7’s to be used in final system
oSLB
uHTR
TPG input to PP not part of test
Test set-up @ 904

## Slide 41: Results compared to objectives - 1
The stability of the MP7 links was extensively tested several times overnight for 8 hours at a time, 72 links operating, monitoring the CRC counters and the alignment flags.
0 CRC errors 0 alignment errors

## Slide 42: Algorithms used in TMT test
Clusters
2x2 clusters
Overlap filtering and e/γ/τ identification logic available but not used
Candidates sorted in φ by ET before output
Sort in η available but not used to increase statistics for validation
Jets
8x8 circular jets (biggest under consideration)
Candidates sorted in φ by ET before output
Sort in η available but not used to increase statistics for validation
Sums
Scalar and vector sum of energy in each φ ring of towers
Number of “towers over threshold” in each ring calculated (potential PU estimator)

## Slide 44: WP3 planning
Issues for calorimeter trigger
  US readiness & funding
    CTP7 for Layer 1 is only at layout stage (just gone to fabrication)
  Planning for 2015
    US proposed short term interim upgrade but all aspects of development (hardware, firmware, software) are late and behind full upgrade planning
    oSLB and oRMs installation in LS1 is crucial for full upgrade
EDR 12 & 13 November
  propose revision of planning when outcome is known
Discussions started for HL-LHC Track-trigger planning
  in Tracker community. MP7/TMT are promising test-bed

## Slide 46: Finances
All RA posts now filled
Expenditure as expected
  continuing orders of MP7 and FC7 prototypes
  µTCA hardware
  materials for 2S-modules and beam test
Looking for OSC feedback on
  financial table format
  how to include CG grant spending
  milestone reporting
  risk register

## Slide 47: Conclusions
The next phase of the project is well on track
  continued good progress
Main issues concern adaptation to LHC schedule
  it is unlikely that there will be much new information about long term schedule and planning very soon
  perhaps at next RRB?
Propose revision of milestones within next six months
  expect feedback from trigger EDR and possible strategic decisions
  evaluate options for Phase II tracker developments

## Slide 48: Further information

## Slide 49: Stub logic features
Cluster width
  exclude clusters wider than 3 strips
Offset correction and correlation
  programmable window, selects pT
    up to +/-8 channels
  programmable offset, adjust lateral displacement
    up to +/-3 channels
n
n+1
n-1
1/2/3 strip
cluster on
channel n
channel
comparator
outputs
p = ∞
IP
R-f view
offset

## Slide 50
analogue front end amplifier
  re-examine pulse shape for dead-time issue
    maybe postamp feedback resistor tweak necessary
  check optimum input transistor dimensions for 5 cm strips
    5 pF was original target
  try and adjust for 1.0 V operation
    can’t guarantee success
comparator
  2 comparators/channel? 5 sigma and 3 sigma thresholds?
    (1 chan > 5s) OR (2 neighbours > 3s)=> hit
      some issues of what to do with comparator outputs
        5/3 sigma pipeline, or 2x pipeline
        what to do with 5 sigma neighbouring 3 sigma (different combinations)
        more signals to cross chip boundaries?
    likely extra 50 uW / channel
biases
  linear enough? monotonic enough? enough resolution?
hit detect
  keep existing circuit but plan to run in variable mode only
  then need additional circuit to suppress hips - if comparator output high for longer than 3 BXs (4 BXs?)
mask to pipeline
  needed somewhere if moving to sparsified system, not necessarily on CBC but probably best place
  can be separate to mask for correlation logic
pipeline
  length increase to 25 usec or thereabouts
  issues of SEU and ionizing sensitivity (if minimum size devices)
trigger rate capability to 1 MHz
output data format
  how many lines at what rate?, differential/single-ended? - baseline 12 lines @ 160 Mbps
offset correction
  4 domains / chip (only 2 in CBC2)
correlation
  +/- 8 channels, ½ strip resolution => 8 bit address
  5 bit bend information
  priority encoding of highest 3 pT stubs (Mephisto)
CBC3
slow ADC?
with “band-gap accuracy” can at least
get an accurate value for the voltage biases
  probably useful but is it worth it?
  probably not if have to develop from scratch

## Slide 51
GLIB
bias
bias
hybrid temp.
stabilisation
(Peltier)
hybrid LV
power (1.2,
3.3, +/-5)
I2C hub
mains
plug
power
supplies
RJ45 cable
(~ 10m )
module test-beam system
can use I2C to monitor
1.2 and 3.3 currents and
hybrid temperatures
+6V
-5V
+5V
+9V

## Slide 52
127
CBC3 - the “final prototype”
bottom
top
8 bits to describe cluster
address in bottom layer
5 bits to describe correlating cluster
address in top layer window
1 or 3 strip
cluster centred
on channel n
2 strip cluster
centred on
n and n+1
n
n+1
n-1
next version of chip should incorporate all features required for HL-LHC
final choices for front end
  ½ strip cluster resolution
    2 strip cluster position assigned to mid-point
stub data definition
  8 bits address (for ½ strip resolution) of cluster in bottom layer
  5 bit bend information
    address of correlating cluster in top layer
stub data formatting & transmission to concentrator
  13 bit / stub, up to 3 stubs/BX => 39 bits
  +1 bit unsparsified L1 triggered readout data
  => 40 bits / 25 nsec
    e.g. 10 lines at 160 Mbps (per chip)
other useful features
  e.g. slow ADC to monitor bias levels
  …
concentrator
CBC
CBC
CBC
CBC
CBC
CBC
CBC
CBC
10 lines / CBC
25 ns
S1
S1
S1
S1
S1
S1
S1
S1
B1
B1
B1
B1
B1
S2
S2
S2
S2
S2
S2
S2
S2
B2
B2
B2
B2
B2
S3
S3
S3
S3
S3
S3
S3
S3
B3
B3
B3
B3
B3
R
25 ns
CBC data to concentrator

## Slide 53: TMT-test setup @ 904
PP - T
PP - B
MP
DEMUX
- 720 Gbps of data going through the MP board
- The MP is processing data from the entire calorimeter

## Slide 54: Floorplan of FPGA
Clusters
Towers
Jets
Sorting
Communication
DAQ
MGT’s
Buffers
Algorithms
Infrastructure

## Slide 55: Resource usage of FPGA
Entire FPGA
 | Infrastructure | Algo + Infrastructure | 
Registers | 9% | 21% | 
LUTs | 19% | 36% | 
DSPs | 0% | 8% | 
BRAM | 12% | 12% | 
 | Infrastructure | 
Registers | 20% | 
LUTs | 35% | 
DSPs | 13% | 
BRAM | 0% | 
Algo area only
All Algos and Infrastructure: 7 hour build-time

## Slide 56: E/gamma Algorithm
Baseline Stage 2 EG algorithm :
  2x2 Trigger Tower clusters
  Cluster position reported to ½ tower precision
  Default isolation region : 5η x 9ϕ towers
Current focus on PU subtraction for isolation
  Need to estimate the 90% percentile of PU ET distribution
  # towers over threshold shown to work well (below)
  Currently evaluating a range of other algorithms
ϕ
η
✦
Efficiency & rate stable with PU using # towers as estimator
ΔR ~ 0.18

## Slide 57: Jet Algorithm
Baseline stage 2 jet algorithm :
  N x N tower circular jets (up to 8x8)
  Approximates a fixed cone algorithm
As for EG, current focus is PU subtraction
  Need to determine mean ET of PU distribution
  EG/jets may need different PU estimation methods
  Range of algorithms under study
  Expect to choose baseline algorithm soon
η
ϕ
7x7 tower circular jet
Performance of different estimators for Nvtx
# towers above threshold
∑ET
ΔR ~ 0.3