## Slide 1
Ajit Kurup, Imperial College London.
An Automated Conditioning System for the MUCOOL Experiments at Fermilab
ABSTRACT
The MUCOOL project aims to study RF cavities for the Neutrino Factory and the Muon Collider. The large emittance muon beams in these accelerators require high-gradient RF cavities at low-frequencies and they need to operate in the presence of relatively strong magnetic fields. MUCOOL is conducting a number of tests on 805MHz and 201 MHz cavities in order to develop a technology that can meet all of these requirements. An automated conditioning system was developed for the 805MHz test program for MUCOOL. This system was designed to replicate the logic a human operator would use when conditioning an RF cavity and to provide automated logging of the conditioning process.
Signal
Generator
Analogue
Oscilloscope
Waveguide
Directional Coupler
Cavity
forward power
reflected power
Fast ~-30dBm
attenuator
(threshold between reflected power peaks)
Fast Switch
(vacc > 6X10^-8 torr ||
2 consecutive breakdowns)
ACNET
Control
Electronics
vacuum probe
voltage probe
Klystron
Modulator
10Hz clock
Power
Amplifier
Signal
Generator
Analogue
Oscilloscope
Envelope
Filter
Klystron
Modulator
Waveguide
Directional Coupler
Cavity
forward
power
reflected
power
10Hz clock
ACNET
Control
Electronics
vacuum probe
voltage probe
Digital
Oscilloscope
Fast ~-30dBm
attenuator
(threshold between reflected power peaks)
Fast Switch
(vacc > 6X10^-8 torr ||
2 consecutive breakdowns)
Power
Amplifier
NEW SETUP
OLD SETUP