## Slide 1: Neutrinos from Stored Muons nSTORM
n physics with a μ storage ring

## Slide 2: Motivation
The idea of using a muon storage ring to produce neutrino beams for experiments is not new
  50 GeV beam – Koshkarev @ CERN in 1974
  1 GeV – Neuffer in 1980
nuSTORM can:
  Address the large Dm2 oscillation regime and make a major contribution to the study of sterile neutrinos
    Either allow for precision study (in many channels), if they exist in this regime
    Or greatly expand the dis-allowed region
  High-Precision n interaction physics program
    ne and ne-bar cross-section measurements
  Provide a technology test demonstration ( m decay ring) and m beam diagnostics test bed
  Provide a precisely understood n beam for detector studies

## Slide 3: Baseline(s)
100 kW Target Station
  Assume 60 GeV proton
    Fermilab PIP era
  Ta target
    Optimization on-going
  Horn collection after target
    Li lens has also been explored
Collection/transport channel
  Stochastic injection of p
  At present NOT considering simultaneous collection of both signs
Decay ring
  Large aperture FODO
  Racetrack FFAG
  Instrumentation
    BCTs, mag-Spec in arc, polarimeter
150 m

## Slide 4: FODO Decay ring
3.8 GeV/c ± 10% momentum acceptance, circumference = 350 m
Alex Bogacz
JLAB

## Slide 5: The Physics Reach

## Slide 6: Assumptions
Nm = (POT) X (p/POT) X ecollection X einj X (m/p) X Adynamic X W
  1021 POT in 5 years of running @ 60 GeV in Fermilab PIP era
  0.1 p/POT (FODO)
  ecollection = 0.8
  einj = 0.8
  m/p = 0.08 (gct X m capture in p ® m decay) [p decay in straight]
  Adynamic = 0.75 (FODO)
  W = Straight/circumference ratio (0.43) (FODO)
This yields » 1.7 X 1018 useful m decays
þ
þ
Ao Liu
Fermilab/UI

## Slide 7: En spectra (m+ stored)
ne
nm-bar
Event rates/100T
at ND hall 50m
from straight with
m+ stored

## Slide 8: Baseline Detector Super B Iron Neutrino Detector: SuperBIND
Magnetized Iron
  1.3 kT
    Following MINOS ND ME design
    1-2 cm Fe plate
    5 m diameter
  Utilize superconducting transmission line for excitation
    Developed 10 years ago for VLHC
  Extruded scintillator +SiPM
20 cm hole
For 6-8 turns
of STL

## Slide 9: Backgrounds
Left: 1 cm plates Right: 2 cm plates
Ryan Bayes
Glasgow

## Slide 10: Raw Event Rates
3+1
Assumption
Appearance channels

## Slide 11: ne ® nm appearance CPT invariant channel to MiniBooNE
2 cm plate

## Slide 12: ne ® nm appearance CPT invariant channel to LSND/MiniBooNE
3+1
Assumption
Chris Tunnell
Oxford

## Slide 13: Required m charge mis-ID rate needed for given sensitivity

## Slide 14: Comments on n beam
Although the primary beam is from m decay, at the beginning of p injection into the first straight, p ® m nm may offer the opportunity to study nm ® ne appearance
  Capture transport line reduces ne background from K decay by factor of roughly 100

## Slide 15: Project Considerations

## Slide 16: Siting Concept
Steve Dixon (Fermilab FESS) will discuss tomorrow

## Slide 17: Preliminary Cost Estimate
Major Components
  Beamline, Target Station & Horn
  Transport line
  Decay ring
  Detectors (Far & Near)
  Project Office
  Total
Basis of Estimation (BOE)
  Took existing facilities (MiniBooNE beam line and target station, MINOS detector, vetted magnet costing models, m2e civil construction costs, EuroNu detector costing, have added all cost loading factors and have escalated to 2012 $ when necessary.
$30M
9
54
18
15
$126M

## Slide 18: Moving Forward
Why we are here

## Slide 19: ® Full Proposal
June 2012 PAC response to nuSTORM presentation
  The combination of a clear resolution of the short-baseline neutrino anomalies, the precise measurements of the neutrino cross sections, and the synergy with neutrino-factory technology makes this a potentially attractive project.
From Pier
  As you see, the Committee was quite intrigued by the possibility of the nuSTORM approach to resolving the short-baseline neutrino anomalies and its being a stepping stone toward use of neutrino-factory technology.
So,
  Although we do not have a mandate ($$$), there is recognition of the power of the concept and encouragement to proceed to a full proposal.
  In addition, nuSTORM has been included in the European Strategy for Particle Physics document.

## Slide 20
Moving forward:
Facility
  Targeting, capture/transport & Injection (Ao Liu, S. Striganov)
    Need to complete detailed design and simulation
    Mike Geelhoed (external beams) – beam line
    AD Mech – Target station
  Decay Ring optimization (Ao Liu)
    Continued study of both RFFAG & FODO decay rings
  Decay Ring Instrumentation (AD Instrumentation – G. Tassotto)
    Define and simulate performance of BCT, Magnetic-spectrometer, etc.
  Produce full G4Beamline simulation of all of the above to define n flux
    And verify the precision to which it can be determined.

## Slide 21
Moving forward:
Detector simulation
  For oscillation studies, continue MC study of backgrounds & systematics
    Start study of disappearance channels
  Event classification in the reconstruction needs optimization.
    Currently assumes "longest track" is interaction muon.
    Plan to assign hits to and fit multiple tracks.
    Vertex definition must also be improved.
    Multivariate analysis.
  For cross-section measurements need detector baseline design
    Learn much from detector work for LBNE & IDS-NF
Produce Full Proposal for June 2013 PAC Mtg.

## Slide 22: nuSTORM: Boiler plate
nuSTORM mailing lists (on listserv.fnal.gov):
  NUSTORM (general collaboration ML)
  NUSTORM_DETECTOR
  NUSTORM_FACILITY
  NUSTORM_SOFTWARE
Setting DocDB & WEB page (Fermilab hosted)

## Slide 23: nuSTORM: Conclusions
The Physics case:
Initial simulation work indicates that a L/E » 1 oscillation experiment using a muon storage ring can confirm/exclude at 10s (CPT invariant channel) the LSND/MiniBooNE result
nm and (ne ) disappearance experiments delivering at the <1% level look to be doable
  Systematics need careful analysis
  Detailed simulation work on these channels has not yet started
Cross section measurements with near detector(s) offer a unique opportunity
The Facility:
Presents very manageable extrapolations from existing technology
  But can explore new ideas regarding beam optics and instrumentation
Offers opportunities for extensions
  Add RF for bunching/acceleration/phase space manipulation
    Provide m source for 6D cooling experiment with intense pulsed beam