## Slide 1: Detector Working Group Summary & Plans

## Slide 2: Far Detector
MIND
  Baseline has not changed
  R&D limited
  Costing in place
  Sensitivity analysis for new Em (10 GeV(ish)) needs to be done
    This is important, but we do not expect surprises

## Slide 3: Near Detectors
Two Options
  HighResMNu (developed for LBNE)
  SciFi
HIResMNu
  Straw tracker, EM Calor, TRD and m spectrometer
  Meets all needs for ND
  Detector technology exists
  Costed

## Slide 4: Near Detectors II
SciFI
  20 stations of scintillating fiber trackers
  5 cm thick active (scintillator) absorbers
  Dipole field
  Also appears to meet NF ND needs
  Little required R&D
  Not yet costed

## Slide 5: I could end here, but we did have an extended discussion regarding the VLENF
First Step towards THE NF?

## Slide 6: Baseline(s)
100 kW Target Station
  Assume 60 GeV proton
    Fermilab PIP era
  Be target
    Optimization on-going
  Li Lens or horn collection after target
Collection/transport channel
  Two options
    Stochastic injection of p
    Kicker with p ® m decay channel
    At present NOT considering simultaneous collection of both signs
Decay ring
  Large aperture FODO
  Racetrack FFAG
  Instrumentation
    BCTs, mag-Spec in arc, polarimeter
108 m

## Slide 7: p production
In momentum range
2.7 < 3.0 < 3.3
Obtain
0.11 p+/pot
0.10 p-/pot
with 60 GeV p
What Fraction of this can we
actually accept and transport?
Sergei Striganov
Fermilab

## Slide 8: FFAG Racetrack
dp/p » 15%
acc-kurri – 1119-01-2011
2 GeV/c
Low dispersion in straight
Lagrange & Mori
Kyoto

## Slide 9: RFFAG Tracking Studies
Akira Sato
Osaka

## Slide 10: Assumptions
Nm = (POT) X (p/POT) X ecollection X einj X (m/p) X Adynamic X W
  1021 POT in 5 years of running @ 60 GeV in Fermilab PIP era
  0.1 p/POT
  ecollection = 0.9
  einj = 0.9
  m/p = 0.08 (gct X m capture in p ® m decay) [p decay in straight]
    Might do better with a p ® m decay channel
  Adynamic = 0.9 (from G4Beamline simulation)
  W = Straight/circumference ratio (0.34)
This yield 2 X 1018 useful m decays

## Slide 11: Experimental Layout
Must reject the
“wrong” sign m with
great efficiency
Appearance
Channel:
ne ® nm
Golden Channel
Why nm ® ne
Appearance Ch.
not possible
100

## Slide 12: Baseline Detector Super B Iron Neutrino Detector: SuperBIND
Magnetized Iron
  1 kT fiducial volume
    Following MINOS ND ME design
    1 cm Fe plate
    5 m diameter
  Utilize superconducting transmission line for excitation
    Developed 10 years ago for VLHC
  Extruded scintillator +SiPM
20 cm hole
For 3 turns
of STL

## Slide 13: Event Rates

## Slide 14: Appearance Channel

## Slide 15: Sensitivity – n mode CPT invariant to LSND/MinBooNE
Chris Tunnell
Oxford

## Slide 16: But……
But, so far, we
Have not reached the
Eff/bkg rej. We want/need
Change Em from 2 GeV
To
3 GeV
Ryan Bayes
Glasgow

## Slide 18: ne Disappearance
Walter Winter
JM-UW

## Slide 19: Outlook
Future Work:
Facility
  Targeting, capture/transport & Injection
    Need detailed design and simulation
  Decay Ring optimization
    Continued study of both RFFAG & FODO decay rings
  Decay Ring Instrumentation
    Define and simulate performance of BCT, polarimeter, Magnetic-spectrometer, etc.
  Produce full G4Beamline simulation of all of the above to define n flux
    And verify the precision to which it can be determined.

## Slide 20: Outlook II
Future Work:
Detector simulation
  For oscillation studies, continue MC study of backgrounds & systematics
    Also investigate disappearance channels
  In particular the event classification in the reconstruction needs optimization.
  For cross-section measurements need detector baseline design
    Learn much from detector work for LBNE & IDS-NF
      Increased emphasis on ne interactions, however
    Near Detector hall could be envisioned as n detector test facility

## Slide 21
VLENF can do both ne and nm disappearance, in both polarities
VLENF can cover ne disappearance best-fit
VLENF outperforms basically any alternative setup ( Sterile neutrino white paper) in which there are 21 experimental possibilities discussed.

## Slide 22: A NF by any other name is still a NF
I have felt strongly that whatever we call this effort, NF should be in the name
However, recent events have changed my mind
What is unique?
  A new way to produce high-energy ns
nSTORM
Neutrinos from STORed Muons
Thanks to Joachim

## Slide 23: Conclusions
nSTORM:
Delivers on the physics for the study of sterile n
  Offering a new approach to the production of n beams and will allow us to confirm/exclude LSND/MiniBooNE n-bar data
Can add significantly to our knowledge of n cross-sections, particularly for ne interactions
Provides an accelerator technology test bed
  But can also utilize existing accelerator infrastructure
Provides a powerful n detector test facility
First step on a long Journey?

## Slide 24: END