## Slide 1: Introduction to CMS
Geoff Hall
University of Bristol
Brunel University
Imperial College London
Rutherford Appleton Laboratory
24 October 2014

## Slide 2: Content
I know that few in the audience are physicists
  so I plan to give only an elementary introduction to the experiment
Main objectives and experimental requirements
  illustrations of some of the items built
Brief history of development and construction
Focus on objects which have been constructed and purchased
  hope to provide some insight into opportunities for business
To be supplemented later by a few more details on electronic procurements
  in a separate session

## Slide 3: What is the Large Hadron Collider?
Latest CERN accelerator started operation 2010
  very high intensity
    1015 collisions per year
  very high rate
    beams cross @ 40MHz
  few “interesting” events
    ~100 Higgs decays per year
  Beams (from 2015)
    6.5 TeV protons
    => 13 TeV energy
      also ions, eg Pb
LHC

## Slide 4: Where is the LHC?
~100m
Alps
Jura

## Slide 5: What are we doing at the LHC?
Colliding beams of protons
  to maximise the energy available to create new particles
u
u
d
u
u
d
proton collisions are actually between their constituent parts…
   ~ 1/p ≈ 1/E
gluons
quarks (≈ real and virtual)
and the particles they exchange (Z, W,…)
proton
proton
(No more physics after this slide!)

## Slide 6: The Compact Muon Solenoid experiment
a general purpose detector for studying the full range of physics at the CERN Large Hadron Collider
  designed to operate (nominally) for 10 years
  high radiation levels throughout the experiment
  they originate with flux of particles originating from the p-p collisions
    so highest in centre and endcap regions
  also operate with heavy ions: ~ 1 month annually
R [cm] | Fast hadron fluence [cm-2] | Dose [kGy] | Dose [Mrad]
4.3 | 246 1013 | 830 | 83
22 | 16 1013 | 67 | 6.7
115 | 2 1013 | 2 | 0.2
Suffice to say, these are very high and comparable with nuclear reactor interiors

## Slide 7: CMS: Compact Muon Solenoid
ECAL
Tracker
HCAL
4T solenoid
Muon chambers
Total weight: 12,500 t
Overall diameter: 15 m
Overall length 21.6 m
Magnetic field 4 T
constructed as a series of layered sub-detectors, each with a specific purpose

## Slide 8: Design philosophy
Large solenoidal (4T) magnet
  iron yoke - returns B field, absorbs particles
Muon detection - penetration
  the only particles we can measure which traverse the whole detector
Calorimeters – absorb Energy
  electromagnetic – electrons and gammas
  hadronic – all other types of particle
Tracking system – bend in B field
  momentum measurements of charged particles
  complex, multi-particle events
  complement muon & ECAL measurements

## Slide 9: From a hole in the ground

## Slide 10: Assembly on the surface

## Slide 11: ECAL crystal scintillators

## Slide 12: Lowering endcap YE+3 Nov 2006

## Slide 13: Lowering magnet and central YB0 Feb 2007

## Slide 14: Endcap muon/forward calorimetry YE-1 Jan 2008

## Slide 15: Vacuum tank December 2007
Services =
gas, optical fibres, power and signal cables, liquids for cooling, etc

## Slide 16: Tracker installation Dec 2007
One of the final detector insertions

## Slide 17: The detectors
Would not exist without commercial procurements
For illustration, I have chosen a couple of examples where there has been a strong UK involvement. Our detector activities have included
  Custom integrated circuit electronics
  Board-based digital electronics
  Silicon sensors
  Vacuum photodiodes
  Scintillating crystals
  Semi-custom optical links
  Mechanical assemblies – some very large
  Data acquisition and software development
  …
In most cases in close collaboration with scientists and engineers from other countries

## Slide 18: CMS Tracker and its sub-systems
TOB
TOB
TID
TID
TIB
TIB
TEC
TEC
PD
PD
Two main sub-systems: Silicon Strip Tracker and Pixels
  pixels quickly removable for beam-pipe bake-out or replacement
  SST not replaceable in reasonable time
Microstrip tracker | Pixels
~210 m2 of silicon, 9.3M channels | ~1 m2 of silicon, 66M channels
73k APV25s, 38k optical links, 440 FEDs | 16k ROCs, 2k olinks, 40 FEDs
27 module types | 8 module types
~34kW | ~3.6kW (post-rad)

## Slide 19: Some milestones of a long project
~Jan 1990 R&D projects
Apr 1992 CMS Letter of Intent
Dec 1994 Technical Proposal
Apr 1998 Tracker Technical Design Report
Oct 1999 Front End Readout ASIC in 0.25µm CMOS
Dec 1999 Decision to construct All Silicon Tracker
Feb 2000 Tracker Technical Design Report Addendum
Apr 2006 Module production completed
Nov 2006 Tracker integration complete
Dec 2007 Tracker inserted in CMS
Mar 2008 Tracker connections completed
  Sep 2008 small interlude
Nov 2009 Tracker ON with LHC beam
Mar 2010 Data taking at 7 TeV
R&D phase

## Slide 20: Electromagnetic Calorimeter
Measures electron and photon locations and energies
  ~80,000 PbWO4 scintillator crystals
  Sensors
    APD (barrel)
    VPT (end cap)
Endcap assembly
25.4 mm
Heavy mechanical engineering
Innovative crystals and photosensors
Demanding modern electronics
Off-detector electronics and services

## Slide 21: ECAL modules
Single endcap
crystal with VPT
Main challenges – as well as radiation tolerance
  CMS ECAL designed for very high energy resolution
    physics advantages for several specific discoveries
  very dense crystal material, with demanding specifications
    precise mechanical assembly and tolerances
    final object very heavy
  electronics crucial
    large signal dynamic range
    (~16bits) & high precision requirement
    low noise
    linearity
    stability
  information vital to trigger
    selects data for readout

## Slide 22: Tracker: APV25 custom integrated circuit
8.1 mm
7.1mm
pipeline
128x192
128 x preamp/shaper
APSP + 128:1 MUX
pipe logic
bias gen.
CAL
FIFO
control
logic
Main features (many innovative, at the time)
  Commercial 0.25µm CMOS
  128 programmable readout channels
  amplifiers, memory, controls,…
Designed and delivered by Imperial College and Rutherford Appleton Lab
  manufacture via CERN contract
digital header
128 analogue samples
APV O/P Frame
Peak
Decon.

## Slide 23: Optical links
System developed for CMS Tracker mainly by CERN with industrial partners – later used for calorimeter, and other detectors
  1.3µm single mode FP laser transmitters, III-V semiconductor Tx & Rx
    good linearity over wide range, good radiation & B-field tolerance

## Slide 24: Tracker - Front End Driver
Monolithic assembly (density/cost)
~ year 2005
in UK with high yield
opto-electric conversion
data processing
data transfer
VME control and slow readout
typical of many other CMS modules
“Primary” Side
OptoRx
CFlash
VME64x
9U board
34 x
FPGAs
Analogue
TTC
FE Unit
Power
Memories
96 channels
JTAG

## Slide 25: Tracker Construction by worldwide effort Austria, Belgium, Finland, France, Germany, Italy, CERN, Switzerland, UK, USA –62 institutes much movement of components and assemblies Sensors, ASICs, hybrids procured and tested some parts commercially: e.g. hybrids Modules constructed in our dedicated centres, using automated assembly methods…

## Slide 26: Modules and sub-system assembly
Endcap petals
(Au, Ge, Be, Fr)
TOB modules and Rods
(US, CERN)
Hybrids (industry)
Inner barrel shells (Italy)

## Slide 27: Sub-system integration

## Slide 28: Integration at Tracker Integration Facility
Dedicated clean room laboratory in CERN
  assembled sub-systems, then added external cables, cooling, …

## Slide 29: Some of the challenges overcome
Sensors: two major contracts with very different production quality
Hybrids: flexible kapton-metal layer structure
  subtle problems in through-via manufacture identified at late stage
ASIC yield: variations after initial very good beginning
  worked with company to understand and solve
Cooling plant performance: manufacture weakness
  failures in plant and components
Many, many other issues
  early attention to minor details is crucial to avoiding costly delays
  most items are highly specialised with few, or no, second sources

## Slide 30: Collision tracks: December 2009
Candidate multi-jet event at 2.36 TeV 4 particle-flow jets with ET > 7 GeV tracks displayed with pT > 0.4 GeV

## Slide 33
Discovery!

## Slide 34: The future
The experiments were demanding to design and build
  the accelerator too…
  but we succeeded in overcoming unprecedented challenges
  a huge effort by many people and institutes, over many years
Now we have set ourselves an even more difficult problem
  upgrade the experiments to take data for a further 10-15 years
  under even more demanding conditions
  radiation tolerance, data volumes, reliability,..
  while maintaining, or even improving, performance
Replacing several major sub-detectors
  and many other improvements
  currently at R&D stage, prototyping, then construction from 2018?